GPSFR: GPS-free Geographic Routing Protocol for Intelligent Vehicles

Qing Yang

Graduate Student

Department of Computer Science and Software Engineering

Auburn University

Abstract

Intelligent vehicles can improve safety by communicating critical road hazard and traffic information among vehicles in the roadway. In this paper, we propose a novel routing protocol called GPS-Free Geographic Routing (GPSFR) for inter-vehicle communication that does not require position information (e.g. from GPS) but instead rely on relative position that can be determined dynamically. Considered the complexity of rural highways, proposed method can solve the problem when vehicles are nearby the interchange, on a curve, trying to merge or leave of the highway. GPSFR greedily chooses the best next hop neighbor based on a Balance Advance (BADV) metric that balances between proximity and link stability due to relative velocity. The simulation demonstrates that by taking relative velocity into account, GPSFRs link breakage frequency is only 27% that of GPSR in the best case, and 70% in the worst case. Furthermore, the average path length of GPSFR is the same as that of GPSR about 80% of the time.

Bio

Qing Yang received the B.E. and M.E. degrees in Computer Science from Nankai University and Harbin Institute of Technology, China, in 2003 and 2005, respectively. He is currently working on his Ph.D. degree in Computer Science and Software Engineering at Auburn University. He is a Vodafone Fellowship recipient at Auburn University in the Department of Computer Science and Software Engineering, Auburn University. His research interests include routing/Mac protocol for vehicular networks, target tracking in sensor networks and distributed systems.