Securing Wireless Networks without Crypto

Wade Trapp

WinLAB, Rutgers University

North Brunswick, NJ

Abstract

Securing wireless networks is distinctly different from securing "wired" networks. In part, this is due to the fact that wireless networks are open: open because the radio medium is a broadcast medium, which means adversaries can easily witness anything that is transmitted; and open because wireless devices are commodity items -adversaries can easily purchase low-cost wireless devices and, with little effort, use these platforms to launch attacks. In spite of these differences, the approach that is commonly taken to secure wireless networks has been to translate traditional, cryptographic network security protocols to the wireless domain. Although the application of conventional cryptographic protocols to wireless networks is essential, such an approach is incomplete - it leaves out the whole wireless aspect! Such an approach cannot capture the full range of threats facing wireless networks, nor can it capture the full spectrum of possible solutions that are available for protecting wireless networks.

Over the past two years, my research group has focused on addressing core security functionalities that don't directly rely on cryptography, but instead utilize the unique features of wireless communications to secure wireless networks. This effort, SEVILLE (Security Via Lower Layer Enforcements), has led to several technological advancements that promise to dramatically alter how we secure wireless networks. At the most basic level, SEVILLE uses the properties of the wireless medium to enhance traditional approaches to authentication and confidentiality. The enabling factor behind SEVILLE is the fact that in the rich multipath environment typical of wireless networks, the response of the medium along any transmit-receive path is frequency-selective (or equivalently dispersive) in a manner that is location-specific. In this talk, we shall examine both physical layer authentication and confidentiality services, provide fundamental theoretical results for both, as well as experimental validation that has been conducted to verify the potential impact of such theory.

Bio

Wade Trappe received his B.A. degree in Mathematics from The University of Texas at Austin in 1994, and the Ph.D. in Applied Mathematics and Scientific Computing from the University of Maryland in 2002. He is currently an associate professor at the Electrical and Computer Engineering Department at Rutgers University, and is Associate Director of the Wireless Information Network Laboratory (WINLAB). His research interests include wireless security, wireless networking, multimedia security, and network security. He has developed several cross-layer security mechanisms for wireless networks, including jamming detection and jamming defense mechanisms for wireless networks, privacy-enhancing routing methods, cross-layer anomaly detection, and physical layer security methods. Dr. Trappe is a co-author of the textbook Introduction to Cryptography with Coding Theory, Prentice Hall, 2001. He is the recipient of the 2005 Best Paper Award from the IEEE Signal Processing Society.  He is a member of the IEEE Signal Processing and Communications societies, a member of the ACM, and has served on program committees for several conferences on security and wireless networking and on wireless sensor networks.