WiMAX (IEEE 802.16) based Hybrid Wireless Networks

Srivathsan Soundararajan

Graduate Student

(Advisor: Prathima Agrawal)

Electrical and Computer Engineering
Auburn University

Abstract

Hybrid networks can be conceived by combining suitably interfaced 802.11 access points (APs) and WiMAX (802.16) backhaul. One of the major problems associated with such networks is the increased communication delay experienced by 802.16 users. For instance, containing such delay is important in maintaining quality of service for VoIP applications. This delay can be substantially decreased by a strategic reduction in the number of active 802.16 subscribers in the network. This talk deals with realizing such reduction by rerouting traffic through lightly loaded 802.11 APs. For doing so, a schedule has to be generated. A scheduling algorithm was designed and its effect on the overall network performance, using end to end packet delay as a metric, was analyzed. For this purpose CBR traffic was used over UDP connections. NS-2 simulations using CBR traffic show significant improvement in end-to-end packet delay.

Bio

Srivathsan Soundararajan is a Graduate student in the Department of Electrical and Computer Engineering at Auburn University, Auburn, AL.  He obtained the Bachelor of Engineering (B.E) degree in Electrical Engineering from Anna University, India in 2006.

Currently, he is a Research Assistant under Dr. Prathima Agrawal.  His current area of research is focused on WiMAX based hybrid wireless networks. He has presented his work as a poster in IEEE Broadnets 2007.