ELEC 2200-002 Digital Logic Circuits 
Fall 2008

Homework 5 Problem

Assigned 10/6/08, due 10/13/08

# Problem 1: A 1-bit full-adder circuit has three inputs, data bits A and B, and a carry bit C. It produces two outputs, sum S and carry CO.

# Specify truth tables for the two outputs.

# Write the canonical SOP forms for the two outputs.

# Using Karnaugh maps, find the minimal SOP forms for the two outputs.

# Synthesize a logic circuit to produce the two outputs using inverting gates.