ELEC 2200-002 Digital Logic Circuits 
Fall 2010

Homework 5 Problems

Assigned 10/5/10, due 10/12/10

# Problem 1: Sketch a transistor-level CMOS circuit schematic for a three-input NAND gate whose logic symbol and truth table are given below:

| Truth table |
| --- |
| Inputs | Output |
| A | B | C | F |
| 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 |
| 0 | 1 | 0 | 1 |
| 0 | 1 | 1 | 1 |
| 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 |
| 1 | 1 | 1 | 0 |

# Problem 2: Sketch a transistor-level CMOS circuit schematic for the automobile ignition function obtained in the class using 14 MOS transistors.

# Problem 3: Derive the truth table for the output switching function C of two variables A and B implemented by the logic circuit in the following gate-level schematic.

# Problem 4: Derive the truth table for the output switching function C of two variables A and B implemented by the circuit in the following transistor-level schematic.

# Text boxes

A

B

C

GND

VDD

C

A

B

F

C

B

A