ELEC 2200-003 Digital Logic Circuits 
Fall 2011

Homework 3 Solution

Assigned 9/12/11, due 9/19/11

# Problem 1:  For 3-bit 2’s complement binary integers, construct 4-bit even and odd parity codes by adding a parity bit in the most significant bit position.

# Problem 2: Consider a set of n-bit binary vectors {Xi} such that for any pair of distinctly different vectors the Hamming distance (HD) ≥ p, where p ≤ n. Suppose, we also have another set of m-bit binary vectors {Yj} such that any pair of them has HD ≥ q, where q ≤ m. We form a new set of (n + m) bit binary vectors {Zij} by concatenating the bits of Xi and Yj. Show that for any pair of vectors Zij and Zkl from the new set, such that i ≠ k and j ≠ l, the HD ≥ p + q.

Problem 3: A digital system uses four symbols, A, B, C and D. For these symbols:

- Define a minimum length binary code. What is the Hamming distance between any pair of codes?

- Define a minimum length binary code such that any single-bit error can be detected. What is the Hamming distance between any pair of codes?

- Define a minimum length binary code such that any one or two bit errors can be detected.

Problem 4: Find the decimal values for the following 32-bit floating point numbers expressed in the IEEE 754 format:

- 0 10000000 10000000000000000000000

- 0 01111111 00000000000000000000000

- 1 10000111 00010001000000000000000