ELEC 2200-002 Digital Logic Circuits 
Fall 2015

Homework 3 Solution

Assigned 9/28/15, due 10/5/15

Problem 1: Prove that the number of elements in a Boolean algebra must be even.

# Answer: 		Postulate 6 requires that every element must have a unique complement that is also in the set. Thus, elements form pairs making the total number of elements to be even.

# Problem 2: For two elements, a and b, of a Boolean algebra, use axioms to prove that:

# Answer:	Proof – Proceed as follows:

# Postulate 5 – distributivity

# Postulate 6 – complement

# Postulate 2 – identity element

# Problem 3: For three variables a, b and c of a Boolean algebra, use Venn diagram to prove that:

# Answer:	Proof – From the Venn diagram:

# ab = P + Q, ac = Q + R, bc = Q + S

# therefore L.H.S. = P + Q + R + b + S + c = b + c

# Hence, L.H.S. = R. H.S. and the result is proven.

# Problem 4: Show that a two-valued switching algebra of variables that can take only two values {0, 1} and contains OR (+) and AND (·) operations is a Boolean algebra. The two operations are defined as follows:

| OR (+) | 0 | 1 |
| --- | --- | --- |
| 0 | 0 | 1 |
| 1 | 1 | 1 |

| AND (·) | 0 | 1 |
| --- | --- | --- |
| 0 | 0 | 0 |
| 1 | 0 | 1 |

# Hint: Verify postulates 1 through 6 of Boolean algebra. One way to verify the correctness of an equation is to use a method called the perfect induction, where the equation is satisfied by all possible combinations of values assigned to the variables occurring in the equation.

# Answer: We examine the postulates of Boolean algebra for the two operations defined in the tables:

# Postulate 1. AND and OR are binary operators, which, when applied to a pair of variable in {0, 1}, produce a result that is also in {0, 1}. It is, therefore, a closed system.

# Postulate 2. The elements 0 and 1 are the identity elements for OR and AND, respectively, because for a variable a assuming any value from {0, 1} satisfies the following equations:

# a + 0 = a	and	a 1= a

# Postulate 3. Both operations are commutative because both tables have diagonal symmetries.

# a + b = b + a	and	a b = b a

# Postulate 4. For three variables a, b and c, associativity means:

# a + (b + c) = (a + b) + c	and	a (b c) = (a b) c

# The correctness of these equations is proven by “perfect induction”. The variables a, b and c can assume eight combinations of values. From the definitions of + and · each expression is evaluated. For example, when a = 0, b = 1, c = 0, the left hand side of the first equation is evaluated as, 0 + (1 + 0) = 0 + 1 = 1; R.H.S. = (0 +1) + c = 1 + 0 = 1; two sides are equal. Similar analysis of each of the other seven combinations shows that the equation is valid for all combination of values.

# Similarly, the correctness of the second equation is proven by perfect induction.

# Postulate 5. Distributivity means,

# a (b + c) = ab + ac	and	a + (bc) = (a + b)(a + c)

# Both equations can be proven by perfect induction.

# Postulate 6. Existence of complement. For any element a, we define another element  such that whenever a takes one of its two values,  assumes the other value. Thus,  is also a binary variable and can be included in the set of variables. From the tables defining the two operations, we find that

# and

# This verifies the existence of  as the complement of a.

# Because all six postulates are true, the switching algebra is a Boolean algebra.

# Problem 5: A house alarm system is designed to sense several conditions represented by binary (0,1) Boolean variables, A, F, M, and W, defined as:

# A	=	1	means alarm is activated (usually when house is unoccupied)

# F	=	1	means smoke is detected

# M	=	1	means motion is detected

# W	=	1	Window or door sensor activated due to a possible break-in

# Write an expression for a Boolean function B(A,F,M,W), such that B = 1 will sound a buzzer when smoke is detected, or when alarm is active and either motion is detected or a break-in occurs. Sketch a relay network to connect a battery to the buzzer.

# Answer: The function B is expressed as follows:

# B	=	(Smoke detected) OR (Alarm active) AND (motion detected OR break-in)

# =	F + A· (M + W)

# A switch network for the alarm buzzer is shown below.

# Text boxes

P

Q

R

a

b

c

S

BUZZER

+

F

A

M

W