ELEC 5200-001/6200-001 (Spring 2016)

Homework 2 Problems

Assigned 2/29/16, due 3/7/16

# Problem 1: Execution times of hardware blocks of a single cycle datapath are as follows:

# Program counter write				  5ps

# Multiplexer			  		  2ps

# Control					  3ps

# Register file read or write			15ps

# Sign extension			  		  2ps

# Shift left by 2			  		  2ps

# Adder or ALU					20ps

# Instruction/data memory read or write	20ps

# All other hardware times can be neglected. Find a lower bound on the cycle time for the program counter.

# Problem 2: Consider the hardware times of major units (all others being negligible) in a datapath as:

# Memory access (read or write)	25ps

# ALU					20ps

# Register file (read or write)		15ps

# Determine minimum clock cycle time, average CPI, and average instruction execution time for single-cycle and multi-cycle datapaths for the following program statistics:

# 10% lw, 10% sw, 40% register-type, 20% branch and 20% jump.

Problem 3:

# Suppose an operation involving register file, memory or ALU each takes 1 time unit. Neglecting the time of all other hardware, how much time will each MIPS instruction take on a single-cycle datapath? Consider R-type, lw, sw, beq and j instructions.

# What will be the execution times for MIPS instructions on a 5-cycle multi-cycle datapath using a clock period of 1 time unit?

# A program contains the following mix of instructions: lw 5%, sw 5%, r-type 70%, branch	10%, jump 10%.

# What is the ratio of single-cycle CPU time to multicycle CPU time for running this program on these datapaths?

Problem 4: Clock rates for single-cycle and multicycle datapaths are given as 1GHz and 5GHz, respectively. The following subroutine is used for estimating performance. The argument register $a0 contains a large positive integer and $a1 contains integer 1.

loop	sub	$a0, $a0, $a1

beq	$a0, $0, done

j	loop

done	jr	$31

Determine:

(a) Average cycles per instruction (CPI) for two datapaths.

(b) How much faster is the multicycle execution of the program (ratio of single-cycle to multicycle execution times)?