Procedure for setting links and running Hitec, Proofs, and Atalanta programs:

Enter user-setup right clicking and navigating through the menu. After the window opens, add hitec under EDA tools section. Save and commit changes and exit X-win.

Next time you start X-win, hitec may be run from any path from your account.

Hitec cannot generate tests for circuits that have XOR or XNOR gates. You may have to model these gates if you are very keen on using hitec

for your test generation. For more details on how to use hitec/proofs see the user’s manual.

For test generation, prepare the netlist of your “circuit” as a bench file named circuit.bench and execute:

$do_hitec circuit	//note that there is no .bench extension given

$level circuit

$faultlist

$equiv

$dominators

$testgen

For using fault simulator, delete the TEST.run file and do the following:

$do_proofs circuit

$level circuit

$faultlist

$equiv

$faultsim

Each time you use hitec/proofs make sure you delete the TEST.run

file to avoid errors.

note: The same procedure may be used to setup ATALANTA ATPG on the sun

machines. For help contact Anand Mudlapur, anand@auburn.edu