VLSI Testing ELEC 7250 Project

Electrical and Computer Engineering, Auburn University

Topic: Derive tests for ISCAS'85 (combinational) and          ISCAS'89 (sequential) circuits

An-jen Cheng

Result from hitec simulation

Combinational Circuits

6	c17	1	   10	         0

214	c432	0.9367	   86	         3.167

320	c880	1	   130	         0.017

514	c499	0.9936	   190	         4.717

546	c1355	0.9949	   194	         2.267

603	c1908	0.9952	   268	         0.883

872	c2670	0.9574	   242	         12.917

1179	c3540	0.9592	   348	         9.833

1726	c5315	0.989	   276	         0.8

2636	c7552	0.9811	   452	         17.233

Gate#	type	coverage   vector	system time

Here are ten different combinational circuits that I simulated with using hitec simulator.

All the circuits that have XOR gates written in that will be replaced by four NAND gates (equivalent circuit) such as c499, c432 and so on.

The following diagrams are the compare of gate number as a function of coverage, vector, and system (CPU) time.

Results for simulation:

For the case, that gate number as a function of coverage instead of c432, c1908, and c3540; we can find that the coverage decrease when the gate number increase.

For gate number as a function of vector, instead of c2670 and c5315, we can find that  the vector increase as the gate number increase, but the two circuit (c2670, c5315) do not effect the curve so much.

For gate number as a function of system (CPU) time, we can figure out that instead of c5315, the system time will increase as gate number increase

Figure 1 Gate numbers of combination circuits as a function of   coverage

Figure 2 Gate numbers of combinational circuit as a function of vector

Figure 3 Gate numbers of combinational circuit as a function system (CPU) time

Sequential Circuits

3	8	1	   s27	                  21	                     0.017

8	61	0.6372	   s208	                 152	                     0.117

14	75	0.8604	   s298	                 220	                     2.217

21	99	0.7419	   s382	                 1359	         21.417

15	101	0.9357	   s344	                 105	                     5.35

15	104	0.9343	   s349	                 102	                     4.883

21	106	0.7877	   s400	                 1460	         14.663

19	107	0.8651	   s641	                 203	                     0.217

6	118	0.8177	   s386	                 273	                     0.133

21	119	0.7089	   s444	                 1253	         35.33

16	122	0.4163	   s420	                 159	                     1.267

19	139	0.8193	   s713	                  96	                     0.813

21	141	0.0919	   s526	                  34	                     69.617

32	241	0.2964	   s838	                  145	         22.05

5	256	0.9565	   s820	                  913	         1.75

5	262	0.9379	   s832	                  1024	         2.217

29	311	0.0825	   s953	                  14	                     1.033

74	490	0.3815	   s1423	       89	                    160.017

6	550	0.9711	   s1488	       1216	          4.367

6	558	0.9628	   s1494	       1015	          2.35

DFF #	gate #	coverage   type                  vector	         system time

Here are the 20 sequential circuits that I simulated with using hitec simulator.

The following diagrams are the compare of gate number as a function of coverage, vector, and system (CPU) time; and DFF number as a function of coverage, vector, and system (CPU) time.

For gate number as a function of coverage, the coverage inclines to decrease as the gate number increase, even there are four abrupt coverage (s1488, s1494, s820, s832).

For gate number as a function of vector, the coverage inclines to increase with the increasing gate number, even though there have some abrupt points.

For gate number as a function of system (CPU) time, the CPU time leans to increase with the increasing gate number, even though there have around six points abrupt

(s641, s386, s713, s420, s1488, s1494)

For DFF number as a function of coverage, vector, and CPU time, because as the sequential circuits that have simulated some of the circuits have the same amount of DFF numbers; therefore, for the circuits that have the same amount of DFF one of them will be picked up as the data point.

For DFF number as a function of vector, instead of two abrupt points (s820, s400), the curve leans to increase slightly with the increase of DFF number.

For DFF number as a function of coverage, the curve inclines to decrease with increasing DFF number, even though three sharp drop point(s208,s420,s953).

For DFF number as a function of CPU time, the curve leans to increase with the increasing DFF number.

Figure 4 Gate numbers of sequential circuit as a function of coverage

Figure 5 Gate numbers of sequential circuit as a function of vectors

Figure 6 Gate numbers of sequential circuits as a function of system (CPU) time

Figure 7 DFF numbers in sequential circuits as a function of coverage

Figure8 DFF numbers in sequential circuits as a function of vectors

Figure 9 DFF numbers in sequential circuit as a function of system (CPU) time