Doubly-Selective Channel Estimation Using Superimposed Training and Discrete Prolate Spheroidal Basis Models

Shuangchi He

Graduate Student

Department of Electrical and Computer Engineering

Auburn University

Abstract

Channel estimation for single user frequency-selective time-varying channel is considered using superimposed training. The time-varying channel is assumed to be well-described by a basis expansion model using discrete prolate spheroidal sequences (DPS-BEM). A periodic (non-random) training sequence is arithmetically added (superimposed) at a low power to the information sequence at the transmitter before modulation and transmission. A two-step approach is adopted where in the first step we estimate the channel using DPS-BEM and only the first-order statistics of the observations. Using the estimated channel from the first step, a Viterbi detector is used to estimate the information sequence. In the second step a deterministic maximum likelihood (DML) approach is used to iteratively estimate the channel and the information sequences sequentially, based on DPS-BEM. Simulations show that the proposed approaches are competitive with time-multiplexed training without incurring data-rate loss.

Bio

Shuangchi He received the B.E. and M.S. degrees in electronic engineering from Tsinghua University, Beijing, China, in 2000 and 2003, respectively. He is currently working toward his Ph.D. degree in electrical engineering at Auburn University.

Since 2003, he has been a Graduate Research Assistant of the Department of Electrical and Computer Engineering, Auburn University. His research interests include channel estimation and equalization, multiuser detection, and statistical and adaptive signal processing and analysis.