Getting Your Bearings Right

Secure Localization Scheme for WLAN

Santosh Pandey

(Advisor: Prathima Agrawal)

Abstract

Estimating the location of wireless users, especially wireless LAN (WLAN) clients, has been an active area of research recently. However, most of the previous schemes in this area do not consider the presence of any malicious user within the network. The growing interest in location based services would necessitate the development of a low-cost localization scheme which is robust against the attacks from these malicious users. This talk gives an overview of location based applications and localization schemes that are currently being pursued for various wireless networks. The focus of this talk is on a low-cost secure localization scheme for WLAN. The proposed scheme is based on the current access point (AP) capability of transmitting at different power levels. The main idea is to leverage this capability of APs so that a unique set of the messages transmitted by various APs can be received at every location in the system. The client is expected to transmit back the received messages to the AP it is associated with. The location of the client is then estimated using the set of messages received from the client. The performance of this scheme and its inherent security capabilities will be discussed along with the implementation of this message based scheme. It has been observed from extensive experiments that this scheme has better localization characteristics as compared to the traditional signal strength based localization schemes.