ELEC 5200-001/6200-001 (Fall 2016)

Homework 1 Problems

Assigned 8/31/16, due 9/7/16

Problem 1: John von Neumann and Alan M. Turing are deemed to have influenced the modern computer architecture. Identify one contribution from each that you consider most significant. In your opinion, which one of these two individuals had greater impact on the development of computer?

Problem 2: Define the Harvard and stored-program architectures. Briefly discuss which do you prefer and why?

Problem 3: Define the phenomenon referred to as von Neumann bottleneck. Compare the IAS and MIPS instruction sets with respect to their effectiveness in dealing with von Neumann bottleneck.

Problem 4: The following table gives an 11-word assembly code written for the IAS computer. Each word contains either a 40-bit constant or two 20-bit (left-L and right-R) instructions. The data contains three 1000-word integer arrays, A(I), B(I) and C(I), starting at memory locations 1001, 2001 and 3001, respectively.

| Memory address | Instruction | Comment |
| --- | --- | --- |
| 0 | 999 | Constant N, initialized to 999 |
| 1 | 1 | Constant, set to 1 |
| 2 | 1000 | Constant, set to 1000 |
| 3L | LOAD M(2000) | Transfer A(1000) from Memory address 2000 to AC |
| 3R | ADD M(3000) | Place A(1000) + [B(1000) from Memory address 3000] in AC |
| 4L | STOR M(4000) | Transfer AC to C(1000) at Memory address 4000 |
| 4R | LOAD M(0) | Load N in AC |
| 5L | SUB M(1) | Decrement N in AC by 1 |
| 5R | JUMP + M(6, 20:39) | Test N, if N ≥ 0, jump to 6R to continue |
| 6L | HALT | Halt otherwise |
| 6R | STOR M(0) | Update N in Memory address 0 |
| 7L | ADD M(1) | Increment AC by 1 |
| 7R | ADD M(2) |  |
| 8L | STOR M(3, 8:19) | Modify memory address in 3L |
| 8R | ADD M(2) |  |
| 9L | STOR M(3, 28:39) | Modify memory address in 3R |
| 9R | ADD M(2) |  |
| 10L | STOR M(4, 8:19) | Modify memory address in 4L |
| 10R | JUMP M(3, 0:19) |  |

Examine this assembly code and determine what result it produces.

Problem 5: Write the machine code (binary) for the program in Problem 5.

Problem 6: What is Turing test? Discuss the outcome of the Turing test of 2014.