ELEC 5200-001/6200-001 Computer Architecture and Design 
Fall 2016

Homework 5 Problems

Assigned 11/04/16, due 11/09/16

Problem 1:

# A one-level cache system contains a SRAM cache that is n times faster than the main memory. The cache has an access time T and its miss rate is m. Show that this system will provide an average memory access speed up of n/(1 + mn). Irrespective of how fast the cache hardware is, show that the speed up has an upper bound 1/m.

# For a two-level cache, show that the average memory access speed up has an upper bound 1/(m1×m2), given that m1 and m2 are the miss rates of L1 and L2 caches, respectively.

Problem 2: To meet the data access time requirement of a computer system its cache is to have a 98% hit rate. However, to reduce the cost and to match speeds of the processor and memory, we use a SRAM of limited capacity as a 1-level cache only to provide a 60% hit rate.

# If the main memory is 70 times slower than the SRAM cache hardware, find the average data access time for the 1-level cache with 60% hit rate, expressed in terms of the cycle time T1 for the cache. Show that the data access would be about twelve times faster if the hit rate was 98%, i.e., cache was larger but still could match the processor speed.

# Suppose a level-2 cache brings the data access time to the required value when the cycle time of the L2 cache is 1.2T1. Determine the minimum hit rate for the L2 cache.

Problem 3: For a two-level cache, the cycle times for L1 and L2 caches and main memory are 1, 10 and 100 clock cycles, respectively. The miss rate of L2 cache is twice that of L1. What should the two miss rates be so that the average data access time of this cache system is 2 cycles?

# Problem 4: A cache must accommodate extra bits besides the data bits. Each block contains tag bits and one valid bit. Show that the ratio of hardware storage bits to data bits in a one-level direct mapped cache is,

# Total bits in cache		  B		W

# −−−−−−−−−−−−−−−   =  1 +  −−− (1 + log2 −−−)

# Data bits in cache		 bw		 w

# Where	W	=	number of words in the main memory

# w	=	number of data words in cache

# B	=	number of blocks in cache

# b	=	word size in bits

# Problem 5: Consider a processor that uses a 32-bit virtual memory address. The memory consists of 32-bit words and is byte addressable. Determine,

# How many bytes the virtual memory can have?

# If the page size is 32KB, then how many records should the page table hold?

# How much data space should physical memory have to hold 32K pages?

# How many bits of storage will be needed in a record of TLB?