ELEC 2200-002 Digital Logic Circuits 
Fall 2008

Homeworks 7 and 8 Problems (Updated)

Assigned 10/31/08, due 11/21/08 (revised date)

- Write a behavioral level VHDL description for a combinational circuit having the following specifications and submit it in your report.

  - The circuit has the following inputs and corresponding data types:

    - func: bit

    - A : signed (4 downto 0)

    - B : signed (4 downto 0)

  - The circuit has the following outputs and corresponding data types:

    - result: signed (4 downto 0)

    - overflow: bit

  - The circuit performs the following function:

    - When (func = ‘0’) 
result = A + B

    - When (func = ‘1’)
result = A – B

    - Flag overflow condition

      - When any of the following conditions occur

        - (A>”00000”) and (B>”00000”) and (func=’0’) and (result<=”00000”) or

        - (A>”00000”) and (B<”00000”) and (func=’1’) and (result<=”00000”) or

        - (A<”00000”) and (B<”00000”) and (func=’0’) and (result>=”00000”) or

        - (A<”00000”) and (B>”00000”) and (func=’1’) and (result>=”00000”)

overflow = ‘1’

      - else

        - overflow = ‘0’

  - “signed” data type declarations are similar to “bit_vector” declarations. Instead of the keyword “bit_vector” you would use the keyword “signed”  Please note that to use the “signed” datatype, you will have to add the following lines at the top of your code:

library IEEE;

use IEEE.std_logic_1164.all;

use IEEE.numeric_std.all;

(Then start your code here)

- Simulate your VHDL description using the tool ModelSim. Apply and simulate following given ten test cases of input combinations and report the input-output simulation results in tabular format. The ten input combinations that you need to simulate are:

  - Input A = 0, Input B = non-zero, func = 1

  - Input A = non-zero, Input B = 0, func = 0

  - Input A = max value, Input B = max value, func = 0

  - Input A = max value, Input B = min value, func = 0

  - Input A = min value, Input B = max value, func = 0

  - Input A = min value, Input B = min value, func = 0

  - Input A = max value, Input B = max value, func = 1

  - Input A = max value, Input B = min value, func = 1

  - Input A = min value, Input B = max value, func = 1

  - Input A = min value, Input B = min value, func = 1

Note:

        - (min value) is the minimum signed binary value that can be represented using 5 bits, which is -24 =  -16 (decimal) = 10000 (binary)

        - (max value) is the maximum signed binary value that can be represented using 5 bits, which is 24 - 1 =  15 (decimal) = 01111 (binary)

        - The operation (result<=”00000”) is a relational operation which means “less than or equal to” and not an assignment operation as it will occur inside an “if” or a “when” statement.

Informational Comment: Note that these ten test cases provide just a partial verification of your design and more test cases can be considered if required. The above given test cases are based on a heuristics of testing corner cases (min-max) for verification of the design.

- Synthesize your behavioral level VHDL code using the tool Leonardo Spectrum to convert it into a structural level net-list. Synthesize the circuit using both types of optimizations; which is area optimized and delay optimized, and save the generated net-lists in Verilog format.

Submit the synthesized net-list for both types of optimizations (area and delay optimizations)

Report the following for both area and delay optimized net-list:

    - No. of gates utilized from the area report

    - The critical path delay from the critical path delay report

- Simulate the synthesized netlists from task no. 3 (again both area and delay optimized) using the tool ModelSim using the same ten test cases as used in task no. 2. Report the input-output simulation results in tabular format.

- Use the automatic test pattern generator (ATPG) tool FlexTest to generate the tests for the area and delay optimized netlists. Report the following for both netlists:

  - No. of stuck-at-faults

  - No. of test vectors generated

  - % fault coverage

  - CPU seconds for test vector generation