ELEC 2200-003 Digital Logic Circuits 
Fall 2011

Homework 6 Solution

Assigned 10/17/11, due 10/24/10

# Problem 1: A house alarm system is designed to sense several conditions represented by binary (0,1) Boolean variables, A, F, M, and W, defined as:

# A	=	1	means alarm is active (usually when everyone leaves home)

# F	=	1	means smoke is detected

# M	=	1	means motion is detected

# W	=	1	Window or door sensor activated due to a possible break-in

# Write an expression for a Boolean function B(A,F,M,W), such that B = 1 will sound a buzzer when smoke is detected, or when alarm is active and either motion is detected or a break-in occurs.

# Give a truth table for B(A,F,M,W) and write the sum of products description.

# Sketch a Karnaugh map of B(A,F,M,W), express the minimized function as sum of largest possible product terms, and minimize the number of literals in the representation.

# Sketch a gate-level implementation using AND and OR gates.

# Sketch a CMOS transistor-level circuit using 14 or fewer transistors. Note that a three NOR gate implementation can be derived from de Morgan’s theorem.