ELEC 2200-002 Digital Logic Circuits 
Fall 2015

Homework 1 Problems

Assigned 9/8/14, due 9/16/14

# Problem 1: Find the decimal values of 5-bit binary strings, 01100, 00110, 11001 and 11000, assuming that their format is (a) signed integer, (b) 1’s complement, or (c) 2’s complement.

Problem 2: Perform binary addition of four-bit binary numbers, 01110 and 11111. Ignore the final carry, if any, to obtain a five-bit result. Determine the decimal values for the two given and the sum binary strings assuming that they are: (a) 2’s complement integers, (b) 1’s complement integers, and (c) signed integers. Verify correctness of the addition for the three cases.

Problem 3: For following four-bit 2’s complement binary integers, perform addition, check overflow and verify correctness of results by converting numbers as decimal integers:

- 0100 + 0100

- 0111 + 1001

# Problem 4: Add the following pairs of 4-bit 2’s complement integers. If an overflow occurs, then expand the numbers to 8-bit representation and add:

# 0101 + 1101

# 1011 + 1101

# 1011 + 1011

# Problem 5: Multiply 4-bit 2’s complement integers, 0110 × 1100, using the direct multiplication (i.e., without separating the signs) of 2’s complement integers. Show the steps of computation.

# Problem 6: Carry out the calculation steps for 4-bit binary division of positive numbers 1000/0101 (i.e., 8/5) using the restoring division algorithm.

# Problem 7: Carry out the calculation steps for 4-bit binary division of positive numbers 1001/0100 (i.e., 9/4) using the non-restoring division algorithm.

# Problem 8:  For 3-bit 2’s complement binary integers, construct 4-bit even and odd parity codes by adding a parity bit in the most significant bit position.

# Problem 9: Consider a set of n-bit binary vectors {Xi} such that for any pair of distinctly different vectors the Hamming distance (HD) ≥ p, where p ≤ n. Suppose, we also have another set of m-bit binary vectors {Yj} such that any pair of them has HD ≥ q, where q ≤ m. We form a new set of (n + m) bit binary vectors {Zij} by concatenating the bits of Xi and Yj. Show that for any pair of vectors Zij and Zkl from the new set, such that i ≠ k and j ≠ l, the HD ≥ p + q.

Problem 10: A digital system uses four symbols, A, B, C and D. For these symbols:

- Define a minimum length binary code. What is the minimum Hamming distance between any pair of codes?

- Define a minimum length binary code such that any single-bit error can be detected. What is the Hamming distance between any pair of codes?

Problem 11: Find the decimal values for the following 32-bit floating point numbers expressed in the IEEE 754 format

- 1 10000000 10000000000000000000000

- 1 01111111 00000000000000000000000

- 0 10000111 00010001000000000000000

Problem 12: Consider the following 32-bit real numbers in the IEEE 754 format,

X = 0 10001001 00000000000000000000000

Y = 0 10000010 01000000000000000000000

- What are decimal values of X and Y?

- Determine X + Y using the binary addition method for real numbers. Express the result in the IEEE 754 format.

- Perform binary multiplication X × Y, expressing the result in IEEE 754 format.