ELEC 2200-002 Digital Logic Circuits 
Fall 2015

Homework 3 Solution

Assigned 10/14/15, due 10/23/15

# Problem 1:

# What is the total number of minterns possible with n Boolean variables?

# How many distinctly different switching functions of four Boolean variables are possible?

# Using the postulates and theorems of Boolean algebra, show that for three binary variables A, B and C,

# Answer:

# For n variables, there are 2n minterms.

# For n variables there are possible switching functions. This number is 65,556 for n = 4.

# We apply distributivity (Postulates 5), invariance (Theorem 1) and consensus (Theorem 9), respectively, in that order to the left hand side:

# Problem 2: Consider Boolean function of three variables, F(a, b, c) = Σ m (3, 4, 5, 6, 7):

# Construct a truth table for this function.

# Show the function on Karnaugh map.

# Minimize the function using Karnaugh map.

# Sketch a logic gate circuit that will implement the minimized function. How many transistors will this circuit require if implemented in CMOS technology?

# Can this function be implemented with fewer transistors? If yes, sketch the most economical gate-level circuit, specifying how many transistors it will need.

# Answer:

# The truth table is as follows:

| Minterm index | Inputs | Output |
| --- | --- | --- |
|  | a | b | c | F |
| 0 | 0 | 0 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 |
| 2 | 0 | 1 | 0 | 0 |
| 3 | 0 | 1 | 1 | 1 |
| 4 | 1 | 0 | 0 | 1 |
| 5 | 1 | 0 | 1 | 1 |
| 6 | 1 | 1 | 0 | 1 |
| 7 | 1 | 1 | 1 | 1 |

# The Karnaugh map is given below:

| 0 | 2 | 6 1 | 4 1 |
| --- | --- | --- | --- |
| 1 | 3 1 | 7 1 | 5 1 |

# From the Karnaugh map, we represent the function using two product terms:

# This function requires three logic gates as shown below:

# This circuit can be implemented with 6 + 6 = 12 transistors

# Reduction in transistors is possible if we use inverting gates. The following circuit is equivalent to the one designed above (circles represent inversions):

The OR gate with inverted inputs, can be replaced by a NAND gate if we apply de Morgan’s theorem. The following circuit is obtained:

This circuit requires 4 + 4 + 2 = 10 transistors.

Problem 3: Express the following three-variable functions as sums of minterms:

Are these functions equivalent?

Answer: The functions are expanded into minterms as follows:

Comparing the sets of minterms, only F2 and F3 are equivalent.

Problem 4: A microwave oven has a user operated on-off switch that controls a Boolean variable S such that S = 0 (off) and S = 1 (on). However, the power in the oven is not turned on as long as the door is open or the oven contains any metallic object in the cooking area. The door has a sensor that generates a Boolean variable D to indicate the state of the door such that D = 0 (open) and D = 1 (closed). The oven has a metal detector that sets a Boolean variable M as follows:

M = 1, when a metal object is present

M = 0, when there is no metal object found

Sketch a transistor-level CMOS circuit to generate a Boolean variable P from S, D and M, such that P = 1 will turn the power on.

Answer:

The variable P is given by:

The circuit that has a NOT gate and an AND gate is shown below.

# Problem 5: A 2’s complement binary adder circuit adds two integers whose most significant bits (MSB) are A and B. The MSB of the sum produced by the adder is C. Give a truth table for a Boolean variable Z that the adder should provide such that Z equals 1 only when an overflow has occurred. Express Z as a sum of products expression.

Answer: The truth table is as follows:

| A | B | C | Z |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 |
| 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 |
| 1 | 0 | 1 | 0 |
| 1 | 1 | 0 | 1 |
| 1 | 1 | 1 | 0 |

SOP Expression:

# Text boxes

a

b

c

a

b

c

F

a

b

c

F

a

b

c

F

M

S  D

P

VDD

GND