ELEC 5200-002/6200-002 Computer Architecture and Design 
Fall 2006

Homework 2 Solution

Assigned 8/28/06, due 9/6/06

Problem 1

- Add comments to the following MIPS code. Assume that $a0 and $a1 are used for the input and initially contain the integers a and b, respectively. Assume that $v0 is used for output.

add	$t0,	$zero,	$zero

loop		beq	$a1,	$zero,	finish

add	$t0,	$t0,	$a0

sub	$a1,	$a1,	1

j	loop

finish		addi	$t0,	$t0,	100

add	$v0,	$t0,	$zero

- Describe in one sentence what this code computes?

# Problem 2:

Suppose a MIPS compiler uses the following pseudoinstructions:

move	$s1, $s2	# $s1 ← $s2

clear	$t5		# $t5 = 0

ble	$t3, $t5, L	# if ($t3 ≤ $t5) go to L

not implemented in the hardware. How will the assembler translate each of these into a minimal sequence of actual MIPS instructions?

# Problem 3:

A procedure uses registers $s1 and $t0. Write the instructions that compiler should include at the beginning and end of the assembly code of the procedure to save and restore registers.