ELEC 5200-002/6200-002 Computer Architecture and Design 
Fall 2006

Homework 8 Solutions

Assigned 11/6/06, due 11/13/06

# Problem 1: Define datapath latency. What is the pipeline latency for:

# Single-cycle datapath with cycle time of T1

# Pipelined datapath with n stages and a cycle time Tn

# Which of these two datapaths has lower latency? Why?

# Problem 2: Define the throughput of a datapath. Derive the throughputs of the following datapaths in MIPS (million instructions per second) for long streams of instructions:

# Single-cycle datapath with cycle time of T1

# Pipelined datapath with n stages and a cycle time Tn

# Which of these two datapaths has higher throughput? Why?

# Problem 3: Consider a single-cycle datapath whose cycle time is T. To reorganize datapath as an n-stage pipeline, the hardware is divided into n nearly equal delay stages. The cycle time for the pipelined datapath is then the largest delay of any stage. Suppose this cycle time is given as (T/n) + (n, where (>0 is a small constant and n ≥ 2. Find the number of stages that will maximize the throughput for long instruction streams.

# If T = 10ns and ( = 0.1ns, what are the throughputs of the single-cycle, 5-stage pipeline, and the optimum pipeline datapaths? Neglect the effect of latency.