ELEC 5200-001/6200-001 Computer Architecture and Design 
Fall 2007

Homework 1 Problems

Assigned 8/27/07, due 9/10/07

Problem 1: The following table gives an 11-word assembly code written for the IAS computer. Each word contains either 40-bit data or two 20-bit (left-L and right-R) instructions. The data also contains three 1000-word integer arrays, A(I), B(I) and C(I), starting in memory locations 1001, 2001 and 3001, respectively.

| Memory address | Instruction | Comment |
| --- | --- | --- |
| 0 | 999 | Variable N, initialized to 999 |
| 1 | 1 | Constant, set to 1 |
| 2 | 1000 | Constant |
| 3L | LOAD M(2000) | Transfer A(1000) from M(2000) to AC |
| 3R | ADD M(3000) | Place A(1000) + [B(1000) from M(3000)] in AC |
| 4L | STOR M(4000) | Transfer AC to C(1000) in M(4000) |
| 4R | LOAD M(0) | Load N in AC |
| 5L | SUB M(1) | Decrement N in AC by 1 |
| 5R | JUMP +M(6, 20:39) | Test N, if N ≥ 0, jump to 6R to continue |
| 6L | HALT | Halt otherwise |
| 6R | STOR M(0) | Update N in M(0) |
| 7L | ADD M(1) | Increment AC by 1 |
| 7R | ADD M(2) |  |
| 8L | STOR M(3, 8:19) | Modify address in 3L |
| 8R | ADD M(2) |  |
| 9L | STOR M(3, 28:39) | Modify address in 3R |
| 9R | ADD M(2) |  |
| 10L | STOR M(4, 8:19) | Modify address in 4L |
| 10R | JUMP M(3, 0:19) |  |

Examine the assembly code and determine what result it produces.

Problem 2: Write the machine code (binary) for the program in Problem 1.