ELEC 5200-001/6200-001 Computer Architecture and Design 
Fall 2009

Homework 4 Problems

Assigned 9/21/09, due 10/5/09

Problem 1: 	The following predesigned hardware cores are available in 90nm CMOS technology:

| Function | Delay (ps) | Energy (nJ) |
| --- | --- | --- |
|  |  | Active (when used by an instruction) | Standby (not used by instruction) |
| Register file | 50 | 10 | 2 |
| ALU or Adder | 200 | 50 | 10 |
| Memory | 100 | 30 | 3 |
| 32-bit register | 50 | 2 | 0 |

Assume that the delay and energy consumption of other hardware is negligible. Find an upper bound on the clock rate at which a single-cycle MIPS datapath can correctly work. Calculate the energy this datapath will consume for R, B and J types of instructions, respectively.

Problem 2: 	Consider two types of MIPS datapaths. The clock rates for single-cycle and multicycle implementations are 250MHz and 1GHz, respectively. The following subroutine is used for estimating the performances. The argument register $a0 contains a very large positive integer (a million or greater):

repeat		beq	$a0, $zero, finish

addi	$a0, $a0, –1

jump	repeat

finish		add	$v0, $a0, $zero

Determine:		(a) Average cycles per instruction (CPI) for two datapaths.

(b) How much faster is the multicycle execution of the program 					(ratio of single-cycle to multicycle execution times)?