ELEC 5200-001/6200-001 (Fall 2010)

Homework 2 Problems

Assigned 9/6/10, due 9/13/10

Problem 1: Given your understanding of relative addressing used by branch instructions, what is the largest number (K) of instructions that can be placed between “here” and “back”:

back:		add	$s0, $s0, $s0

. . . K instructions . . .

here:		beq	$s0, $s2, back

Problem 2: Implement the following pseudoinstructions using the MIPS core instructions (include comments with your code):

- max	$t0, $s0, $s1	# $t0 takes larger of the contents of $s0 and $s1

- swap	$t0, 100($s0)	# swap contents of $t0 and memory word addressed in $s0

Problem 3: While expanding a MIPS pseudoinstruction the assembler must use (check all that apply):

- ( MIPS core instructions

- ( Any temporary registers

- ( Only the registers specified in the pseudoinstruction

- ( Only $1

- ( $1 and all registers specified in the pseudoinstruction

Problem 4: A main program instruction located at word address 12,000 in the memory calls the procedure SUB that begins at word address 5000.

  - When “call SUB” is executed, what are the contents of $PC and $ra?

  - The main program requires that registers t4, s2 and s3 be not changed by SUB. What actions, if any, should it take before calling SUB and upon return from SUB.

  - The procedure SUB uses all temporary registers and the saved register s0. Does it need to save and restore any registers? If yes, which ones?