ELEC 5200-001/6200-001 (Fall 2010)

Homework 4 Problems

Assigned 9/27/10, due 10/4/10

# Problem 1: MIPS instruction set has an instruction, nop, that does nothing:

# What are the opcode and the 32-bit binary format for nop?

# How is nop executed in a single-cycle datapath?

# How many cycles will nop take in a multicycle datapath?

# Can nop instruction be modified for execution in two cycles on a redisigned multicycle datapath? If yes, how?

Problem 2: Consider a move instruction with two argument registers, $src and $dst, that transfers data from $src to $dst. This instruction is not implemented in the MIPS hardware and is executed as a pseudoinstruction.

- How many cycles will move take on a multicycle MIPS datapath?

- If this instruction is implemented as a hardware instruction, can it be executed in three cycles? If yes, explain how?

- Can this instruction be executed in less than three cycles?

Problem 3:

# Suppose operations involving register file, memory or ALU take one time unit each. Neglecting the time of all other hardware, how much time will each MIPS instruction take on a single-cycle datapath? Consider R-type, lw, sw, beq and j instructions.

# What will be the execution times for MIPS instructions on a 5-cycle multi-cycle datapath using a clock period of 1 time unit?

# It is required to execute the j instruction in two cycles on the multi-cycle datapath? How will you do it?

# A program contains the following mix of instructions:

# Memory operations	10%, equally divided between lw and sw

# R-type			70%

# Branch			10%

# Jump			10%

# What is the single-cycle CPU time to multicycle CPU time ratio for running this program on the two datapaths?