ELEC 5200-001/6200-001 (Fall 2012)

Homework 3 Problems

Assigned 9/19/12, due 10/1/12

# Problem 1: Execution times of hardware blocks of a single cycle datapath are as follows:

# Multiplexer			  2ps

# Control			  2ps

# Register file read or write	10ps

# Sign extension			  1ps

# Shift left by 2			  1ps

# Adder or ALU			20ps

# Instruction or data memory	15ps

# All other hardware times can be neglected. Find a lower bound on the cycle time for the program counter.

# Problem 2: Consider the hardware times of major units (others being negligible) in datapath as:

# Memory access (read or write)	100ps

# ALU					  75ps

# Register file (read or write)		  50ps

# Determine minimum clock cycle time, average CPI, and average instruction execution time for single-cycle and multi-cycle datapaths for the following program statistics:

| Instruction type | Percentage in a program | Average cycles used by instruction |
| --- | --- | --- |
|  |  | Single-cycle | Multi-cycle |
| lw | 20 | 1 | 5 |
| sw | 10 | 1 | 4 |
| branch | 10 | 1 | 2 |
| jump | 10 | 1 | 2 |
| register | 50 | 1 | 4 |

Problem 3:

# Suppose operations involving register file, memory or ALU take one time unit each. Neglecting the time of all other hardware, how much time will each MIPS instruction take on a single-cycle datapath? Consider R-type, lw, sw, beq and j instructions.

# What will be the execution times for MIPS instructions on a 5-cycle multi-cycle datapath using a clock period of 1 time unit?

# A program contains the following mix of instructions:

# Memory type		20%, equally divided between lw and sw

# R-type			50%

# Branch			15%

# Jump			15%

# What is the single-cycle CPU time to multicycle CPU time ratio for running this program on the two datapaths?

Problem 4: Implement the control logic for a single-cycle processor that executes MIPS instructions: lw, sw, R-type, beq and j. Use CMOS gates and minimize hardware in terms of the number of transistors, counting two transistors per input for an inverting (NAND, NOR, NOT) gate. Sketch a logic schematic of your circuit.