ELEC 5200-001/6200-001 (Fall 2012)

Homework 4 Problems

Assigned 10/1/12, due 10/8/12

Problem 1: Consider two types of MIPS datapaths. The clock rates for single-cycle and multicycle implementations are 200MHz and 1GHz, respectively. The following subroutine is used for estimating the performances. The argument register $a0 contains a very large positive integer (1 million or greater):

repeat		beq	$a0, $zero, finish

addi	$a0, $a0, –1

jump	repeat

finish		add	$v0, $a0, $zero

Determine:

(a) Average cycles per instruction (CPI) for two datapaths.

(b) How much faster is the multicycle execution of the program (ratio of single-cycle to multicycle execution times)?

# Problem 2: 	Sketch a schematic showing a multicycle MIPS datapath for the execution of the jump and link (jal) instruction. In your schematic you may include only those units that participate in the execution of this instruction.

Problem 3:	The control for a multicycle MIPS datapath is implemented as a finite-state machine. Suppose, all possible 6-bit opcodes are classified into one of five types:

1.	load or store

2. 	R-type

3. 	Branch type

4. 	Jump type

5. 	Illegal

All illegal opcodes require the same action, i.e., exception, for which the control signals required by the datapath have been determined. Illustrate what modification you will make to the state diagram.

Suppose the FSM is implemented with random logic and four flip-flops. Suggest a state assignment to reduce the dynamic power consumption, assuming that R-type is the most frequently executed instruction.