ELEC 5200-001/6200-001 Computer Architecture and Design 
Fall 2012

Homework 7 Problems

Assigned 10/29/12, due 11/5/12

Problem 1:

# A one-level SRAM cache has n times shorter cycle time compared to the main memory. Show that it will provide an average memory access speed up of n/(1+mn), where m is the miss rate. Show that irrespective of how fast the cache is the speed up cannot be greater than 1/m.

# Show that the average memory access speed up has an upper bound 1/(m1×m2), where m1 and m2 are the miss rates of L1 and L2 caches, respectively.

# Problem 2: A cache system speeds up the memory operation. Suppose a one-level cache is made of memory hardware that is n times faster than the main memory, where n >> 1. Compare the memory speed up with cache to Amdahl’s law, specifically discussing that the hit ratio h and the enhanced fraction fenh play similar roles.

Problem 3: For a two-level cache, the data access times for L1 and L2 caches and main memory are 1, 10 and 100 clock cycles, respectively. Both L1 and L2 caches have the same hit ratio h. What should h be so that the average data access time of this cache system is 3 cycles?

# Problem 4: Consider a processor that uses a 32-bit virtual memory address. The memory consists of 32-bit words and is byte addressable. Determine,

# How many bytes the virtual memory can have?

# If the page size is 16KB how many records should the page table hold?

# How much data space physical memory should have to hold 32K pages.

# Problem 5: A cache must accommodate extra bits besides the data bits. Each block contains tag bits and one valid bit. Show that for 32 bit data words, the ratio of the hardware storage bits to data bits in cache can be expressed as,

# Cache hardware bits		  B		W

# −−−−−−−−−−−−−−−   =  1 +  −−− (1 + log2 −−−)

# Data bits in cache		 bw		 w

# Where	W	=	number of words in the main memory

# w	=	number of data words in cache

# B	=	number of blocks in cache

# b	=	word size in bits