ELEC 5200-001/6200-001 (Fall 2015)

Homework 2 Problems

Assigned 9/8/15, due 9/16/15

Problem 1: Write the MIPS instructions that produce the following binary code. Interpret the action of each instruction:

- 000000 00000 01000 01000 00000 100000

- 000000 01001 00000 01001 00000 100010

- 000000 00000 00000 00000 00000 000000

- 000000 00000 00000 00000 00111 000000

Problem 2: Consider the MIPS pseudoinstruction,

itemp	$r

where $r can be any saved or temporary register. It initializes all temporary registers to the data in $r. How will an assembler expand this into a set of “real” instructions?

Problem 3: The following pseudoinstruction copies the content a memory word whose addresses is in register $s1 to another memory word whose address is register $s2:

mcopy	$s1, $s2

How should a MIPS assembler translate it into a set of real instructions?

Problem 4:

- Add comments to the following MIPS code. Assume that $a0 and $a1 are used for the input and initially contain positive integers a and b, respectively. Assume that $v0 is used for output.

add	$t0,	$0,	$0

loop		beq	$a1,	$0,	finish

add	$t0,	$t0,	$a0

addi	$a1,	$a1,	– 1

j	loop

finish		add	$v0,	$t0,	$0

jr	$ra

- Describe in one sentence what this code computes?

Problem 5: A program uses registers 15 through 24. It calls a procedure. Write the instructions that compiler should include in the program before and after the call.