ELEC 5200-001/6200-001 (Fall 2015)

Homework 3 Problems

Assigned 9/28/15, due 10/2/15

# Problem 1: Execution times of hardware blocks of a single cycle datapath are as follows:

# Program counter write				  7ps

# Multiplexer			  		  2ps

# Control					  3ps

# Register file read or write			15ps

# Sign extension			  		  2ps

# Shift left by 2			  		  2ps

# Adder or ALU					20ps

# Instruction/data memory read or write	25ps

# All other hardware times can be neglected. Find a lower bound on the cycle time for the program counter.

# Problem 2: Consider the hardware times of major units (others being negligible) in a datapath as:

# Memory access (read or write)	20ps

# ALU					20ps

# Register file (read or write)		20ps

# Determine minimum clock cycle time, average CPI, and average instruction execution time for single-cycle and multi-cycle datapaths for the following program statistics:

| Instruction type | Percentage in the program | Clock cycles used by instruction |
| --- | --- | --- |
|  |  | Single-cycle | Multi-cycle |
| lw | 10 | 1 | 5 |
| sw | 10 | 1 | 4 |
| branch | 20 | 1 | 3 |
| jump | 20 | 1 | 3 |
| register | 40 | 1 | 4 |

Problem 3:

# Suppose an operation involving register file, memory or ALU each takes 1 time unit. Neglecting the time of all other hardware, how much time will each MIPS instruction take on a single-cycle datapath? Consider R-type, lw, sw, beq and j instructions.

# What will be the execution times for MIPS instructions on a 5-cycle multi-cycle datapath using a clock period of 1 time unit?

# A program contains the following mix of instructions:

# lw			5%

# sw			5%

# R-type			60%

# Branch			15%

# Jump			15%

# What is the single-cycle CPU time to multicycle CPU time ratio for running this program on two datapaths?

Problem 4: Clock rates for single-cycle and multicycle datapaths are given as 250MHz and 1GHz, respectively. The following subroutine is used for estimating performance. The argument register $a0 contains a very large positive integer (assume several million).

loop	addi	$a0, $a0, –1

beq	$a0, $0, done

j	loop

done	jr	$31

Determine:

(a) Average cycles per instruction (CPI) for two datapaths.

(b) How much faster is the multicycle execution of the program (ratio of single-cycle to multicycle execution times)?