ELEC 5200-001/6200-001 Computer Architecture and Design 
Spring 2007

Homework 7 Solutions

Assigned 4/2/07, due 4/11/07

# Problem 1: Single-cycle datapath

# Modern CMOS technologies allow dual supply voltage operation. This means cores operating at different supply voltages can be integrated on the same chip. Following cores are available for implementing a datapath chip

# :

| Core function | VDD = 2V | VDD = 1V |
| --- | --- | --- |
|  | Delay | Energy per input | Delay | Energy per input |
| Memory | 100ps | 9μJ | 200ps | 3μJ |
| Register file | 50ps | 9μJ | 100ps | 3μJ |
| ALU | 50ps | 9μJ | 100ps | 3μJ |

- What is the minimum clock cycle time for a single-cycle MIPS datapath when all units operate with 2V supply?

- What is the CPI (cycles per instruction) rating for this single-cycle datapath?

- Can you use dual-voltage operation to reduce the power consumption of the single-cycle datapath without reducing its performance?

# Problem 2: Multi-cycle data-path

- What is the minimum clock cycle time for a multi-cycle MIPS datapath implemented with cores given in Problem 1 when a single supply voltage of 2V is used?

- Assuming that all five types of instructions (lw, sw, R-type, branch, and jump) occur with equal frequency what will be the CPI for this multi-cycle datapath?

- Explain whether you can use the low-voltage cores of Problem 1 in a dual-voltage operation to save power without affecting the performance of the multi-cycle data-path? How much energy will each type of instruction save by such a design?

# Problem 3: Multi-cycle control

# In the class, the ten states of finite-state machine (FSM) were encoded 0000 through 1001. Suppose the FSM is constructed using four flip-flops and a CMOS combinational logic block. Assume that the energy consumption of the FSM is proportional to the number of transitions (activity) in flip-flops. Find a state encoding that will, on an average, save at least 30% power when the frequency of instructions is lw 10%, sw 10%, R-type 70%, B-type 5% and J-type 5%.