ELEC 5200-001/6200-001 Computer Architecture and Design 
Spring 2008

Homework 4

Assigned 2/20/08, due 2/27/08

# Problem 1: 		A single-cycle MIPS datapath is designed to execute the simple 	unconditional jump (j) instruction. What extra hardware, if any, will you 	add for the execution of the jump and link (jal) instruction? Give a 	schematic in which you may include only those units that participate in the 	execution of the jal instruction

# Problem 2: 	A single-cycle MIPS datapath contains memories, ALU and register file 			each requiring within 10ns to operate. The delay of other hardware is 			negligible. The processor is being designed for an instruction-specific 			(variable period) clocking using a fundamental external clock of period 			10ns. Thus, the datapath clock period will be an instruction-specific 			multiple of 10ns. How many 10ns cycles should each type of instruction 			be given? Give the logic design for a clock generating circuit that will 			produce a clock signal for the program counter from the 10ns clock.

Problem 3:	Which instruction takes longest to execute in a multi-cycle MIPS 				datapath? Suggest a possible way to reduce its execution by one cycle.