ELEC 5200-001/6200-001 Computer Architecture and Design 
Spring 2009

Homework 2 Problems

Assigned 2/2/09, due 2/13/09

Problem 1: It is decided to quadruple the size of the main memory of the IAS computer. The words are still 40 bits wide. What changes, if any, are required in the opcodes of the instruction set? If we were to add new instructions to the larger memory system, how many more instructions can be added?

Problem 2: Examine the IAS and MIPS instruction sets and tabulate the following:

- Number of instructions.

- Percentage of instructions requiring data access from the memory.

Problem 3: Pseudoinstructions are not part of MIPS instruction set but often appear in MIPS programs. For each pseudoinstruction in the following table, fill in a minimal sequence of actual MIPS instructions in the last column. You may have to use $at for some of the sequences. In the table, big refers to a number that requires 32 bits to represent and small needs 16 bits.

| Pseudoinstruction | What it accomplishes | MIPS | implementation |
| --- | --- | --- | --- |
| move $t1, $t2 | $t1 | = $t2 |  |  |
| clear $t0 | $t0 | = 0 |  |  |
| beq $t1, small, L | if($t1 == small) go to L |  |
| beq $t2, big, L | if ($t2 == big) go to L |  |
| li $t1, small | $t1 = small |  |  |
| li $t2, big | $t2 = big |  |
| ble $t3, $t5, L | if ($t3 <= $t5) go to L |  |
| bgt $t4, $t5, L | if ($t4 > $t5) go to L |  |
| bge $t5, $t3, L | if ($t5 >= $t3) go to L |  |
| addi $t0, $t2, big | $t0 = $t2 + big |  |
| lw $t5, big($t2) | $t5 = Memory[$t2 + big] |  |  |

Problem 4: Given your understanding of relative addressing used by branch instructions, explain why an assembler might have problems directly implementing the branch in the following code sequence:

here:		beq	$s0, $s2, there

. . . many instructions . . .

there		add	$s0, $s0, $s0