ELEC 5200-001/6200-001 (Spring 2011)

Homework 3 Problems

Assigned 2/21/11, due 2/28/11

Problem 1:

# Suppose operations involving register file, memory or ALU take one time unit each. Neglecting the time of all other hardware, how much time will each MIPS instruction take on a single-cycle datapath? Consider R-type, lw, sw, beq and j instructions.

# What will be the execution times for MIPS instructions on a 5-cycle multi-cycle datapath using a clock period of 1 time unit?

# A program contains the following mix of instructions:

# Memory operations	20%, equally divided between lw and sw

# R-type			60%

# Branch			10%

# Jump			10%

# What is the single-cycle CPU time to multicycle CPU time ratio for running this program on the two datapaths?

# Is it possible to execute the j instruction in two cycles on a redesigned multi-cycle datapath? If yes, how will you do it?

Problem 2: 	Consider two types of MIPS datapaths. The clock rates for single-cycle and multicycle implementations are 200MHz and 1GHz, respectively. The following subroutine is used for estimating the performances. The argument register $a0 contains a very large positive integer (1 million or greater):

repeat		beq	$a0, $zero, finish

addi	$a0, $a0, –1

jump	repeat

finish		add	$v0, $a0, $zero

Determine:		(a) Average cycles per instruction (CPI) for two datapaths.

(b) How much faster is the multicycle execution of the program 					(ratio of single-cycle to multicycle execution times)?

# Problem 3: 	Sketch a schematic showing a multicycle MIPS datapath for the execution of the jump and link (jal) instruction. In your schematic you may include only those units that participate in the execution of this instruction.

Problem 4:	The control for a multicycle MIPS datapath is implemented as a finite-state machine. Suppose, all possible 6-bit opcodes are classified into one of five types:

1.	load or store

2. 	R-type

3. 	Branch type

4. 	Jump type

5. 	Illegal

All illegal opcodes require the same action, i.e., exception, for which the control signals required by the datapath have been determined. Illustrate what modification you will make to the state diagram.

Suppose the FSM is implemented with random logic and four flip-flops. Suggest a state assignment to reduce the dynamic power consumption, assuming that R-type is the most frequently executed instruction.