ELEC 5200-001/6200-001 (Spring 2011)

Homework 4 Problems

Assigned 3/7/11, due 2/21/11

Problem 1: It is given that Tm is the time required for reading or writing the memory, Tf  is the time for reading or writing the register file, Ta is the critical path delay of an ALU or adder circuit and Tr is the clock to Q delay of all registers. Derive an expression for lower bounds on the cycle times for single-cycle, multicycle and pipeline MIPS datapaths.

# Problem 2: Assume that each pipeline register and the program counter have a delay of 20ps. Times taken by other major hardware units in a MIPS processor are:

Memory read or write		200ps

Register file read and write	150ps

ALU				230ps

Add unit			200ps

All other hardware, including the control and multiplexers, has negligible delay. Then

# What is the maximum clock frequency for a five-stage MIPS pipeline datapath?

# Neglecting any hazards and resulting stalls, what are the pipeline latency and the cycles per instruction (CPI) for a long instruction sequence?

# Compare this datapath with a single cycle datapath:

| Datapath | Clock cycle time | Clock frequency | CPI | Time per instruction | Million instructions per second (mips) |
| --- | --- | --- | --- | --- | --- |
| Single-cycle |  |  |  |  |  |
| Pipeline |  |  |  |  |  |

# Problem 3: A single-cycle datapath is a one-stage pipeline. It consists of combinational and asynchronous circuitry and a single clocked register, the program counter. Its total cycle time consists of times q required by the register and h used by the rest of the circuitry:

# Assume that the hardware portion of delay h can be partitioned into n equal delay stages separated by clocked registers each having delay q, the first stage register being the program counter. Neglecting the latency and any occurrence of hazards, compute the execution time of an instruction by this n-stage pipeline.

# Show that the performance limit for the pipeline when we neglect the latency and hazards is determined by the register delay q. Find an upper bound for the clock frequency of this pipeline datapath.

# For an n-stage pipeline, suppose the average hazard penalty is α(n – 1) cycles per instruction, where 0 < α < 1.0 and n ≥ 1. Find the optimum number of pipeline stages.

# For a hardware design it is estimated that q = h/25 and for the ISA, α ≈ 0.2, what is the optimum number of stages for this pipeline and what is the corresponding speed up over a single-cycle datapath?

# For q = 20ps, tabulate clock cycle time, clock rate, average CPI and performance in million instructions per second for single-cycle datapath and the pipeline datapath with optimum number of stages found in (d).

# Problem 4:

# (a) Does a five stage MIPS pipeline execution of the following sequence of instructions generate a hazard? If yes, what type of hazard is it?

# sub	$s0, $t0, $t1

# sub	$t2, $s0, $t3

# (b) If the instruction stream in (a) generates a hazard, could it be handled without a pipeline stall? Illustrate the handling of hazard by a sketch of pipeline stages.

# Problem 5: Consider the following MIPS instructions being executed on a five-stage pipeline:

sw    $6, 0($7)                      # Mem[$7] = $6

lw    $8, 0($7)                      # $8 = Mem[$7]

add  $9, $8, $2                     # $9 = $8 + $2

How will a compiler modify these instructions for a pipeline that is implemented without forwarding and hazard detection hardware? Note that to obtain most performance the compiler must avoid any increase in the number of instructions unless absolutely essential.

# Text boxes

Reg.

q

h