ELEC 5200-001/6200-001 (Spring 2012)

Homework 10 Problems

Assigned 4/18/12, due 4/25/12

# Problem 1: The control of a five-cycle multicycle MIPS processor is a finite state machine with 30 states. The instruction set has 96 instructions and contains a six-bit opcode. For a microprogrammed control:

# What should be the size of microPC?

# How many words should the microcode memory have?

# The control may contain one or more dispatch ROMs. How many words should a dispatch ROM have? What should be its word size?

# Problem 2: A virtual memory has a page size of 1024 words, 8 virtual pages, and 4 physical pages. The page table is as follows:

| Valid bit | Virtual page number | Page location |
| --- | --- | --- |
| 1 | 0 | Physical page 3 |
| 1 | 1 | Physical page 1 |
| 0 | 2 | Disk address |
| 0 | 3 | Disk address |
| 1 | 4 | Physical page 2 |
| 0 | 5 | Disk address |
| 1 | 6 | Physical page 0 |
| 0 | 7 | Disk address |

# For the following virtual addresses find the corresponding physical addresses: 0, 3728, 1023, 1024, 1025, 7800, and 4096. Indicate which addresses will cause a page fault.

# Problem 3: A computer has 16 pages of virtual memory but only four physical pages. Initially, the memory is empty. A program references the virtual pages in the order 0, 7, 2, 7, 5, 8, 9, 2, 4. Which references will cause page fault when the page replacement strategy is,

# LRU, or

# FIFO?

# Which strategy produces fewer page faults?

# Problem 4:

# For a sequence of instructions A and B where B follows A, define RAW, WAR and WAW dependences? How do they influence the issuing of B for an out-of-order processing.

# Examine the following sequence of three instructions for out-of-order issue:

# #1	R6 = R5 + R6

# #2	R1 = R5 + R7

# #3	R2 = R1 + R6

# #4	R3 = R5 – R6

# Can #2 be issued in the same cycle as #1? If not when should #2 be issued?

# Can #3 be issued before #1 or #2 is retired? If not, when should #3 be issued?

# Can #4 be issued either together with or before #1, 2 or 3? Explain.

# Problem 5: What are RAW, WAR and WAW dependences? Examine the following sequence of three instructions for out-of-order issue:

# #1	R1 = R5 + R6

# #2	R2 = R1 + R6

# #3	R3 = R5 – R6

# Can #2 be issued in the same cycle as #1? Explain.

# Can #3 be issued either together with or before #2? Explain.