ELEC 5200-001/6200-001 Computer Architecture and Design 
Spring 2012

Homework 7 Problems

Assigned 3/26/12, due 4/2/12

# Problem 1: The control of a five-cycle multicycle MIPS processor is a finite state machine with 30 states. The instruction set has 96 instructions and contains a six-bit opcode. For a microcoded control:

# What should be the size of microPC?

# How many words should the microcode memory have?

# The control may contain one or more dispatch ROMs. How many words should a dispatch ROM have? What should be its word size?

Problem 2: Every microinstruction corresponds to one state in the state diagram with one exception. Why are there two separate states corresponding to RegWr? Can they be combined into a single state?

Problem 3: Suppose in a MIPS instruction set all instructions can be classified into five types, namely, load, store, register, branch and jump. Design the state diagram of a microcoded control for a multicycle datapath using only one dispatch ROM.  Sketch the state diagram showing an appropriate state assignment.

Problem 4: List microinstructions of Problem 3 specifying their functions and sequencing values.