## Slide 1: Modeling & Simulating ASIC Designs with VHDL
Reference: Smith text: Chapters 10 & 12

## Slide 2: Digital ASIC Design Flow
Behavioral
Model
VHDL/Verilog
Gate-Level
Netlist
Transistor-Level
Netlist
Physical
Layout
Map/Place/Route
DFT/BIST
& ATPG
Verify
Function
Verify
Function
Verify Function
& Timing
Verify
Timing
DRC & LVS
Verification
IC Mask Data/FPGA Configuration File
Standard Cell IC
& FPGA/CPLD
Synthesis
Test vectors
Full-custom IC
Front-End
Design
Back-End
Design

## Slide 3: ASIC CAD tools available in ECE
Modeling and Simulation
  Questa ADMS = Questa+Modelsim+Eldo+ADiT (Mentor Graphics)
  Verilog-XL, NC_Verilog, Spectre (Cadence)
Design Synthesis (digital)
  Leonardo Spectrum (Mentor Graphics)
  Design Compiler (Synopsys), RTL Compiler (Cadence)
Design for Test and Automatic Test Pattern Generation
  Tessent DFT Advisor, Fastscan, SoCScan (Mentor Graphics)
Schematic Capture & Design Integration
  Design Architect-IC (Mentor Graphics)
  Design Framework II (DFII) - Composer (Cadence)
Physical Layout
  IC Station (Mentor Graphics)
  SOC Encounter, Virtuoso (Cadence)
Design Verification
  Calibre DRC, LVS, PEX (Mentor Graphics)
  Diva, Assura (Cadence)

## Slide 4: Questa ADMS Analog, Digital, Mixed-Signal Simulation
Questa ADMS
Working
Library
Design_1
Design_2
VITAL
IEEE 1164
Resource
Libraries
Simulation
Setup
EZwave
Input
Stimuli
VHDL,Verilog,
VHDL-AMS, Verilog-AMS,
SPICE Netlists
Eldo,
Eldo RF
Modelsim
View Results
ADiT
Analog
(SPICE)
Digital
(VHDL,Verilog)
Mixed Signal
(VHDL-AMS,
Verilog-AMS)
SPICE
models
Xilinx
SIMPRIMS
Module
Generators

## Slide 5: Hardware Description Languages
VHDL = VHSIC Hardware Description Language
(VHSIC = Very High Speed Integrated Circuits)
  Developed by DOD from 1983 – based on ADA
  IEEE Standard 1076-1987/1993/2002/2008
  Based on the ADA language
Verilog – created in 1984 by Philip Moorby of Gateway Design Automation (merged with Cadence)
  IEEE Standard 1364-1995/2001/2005
  Based on the C language
  IEEE P1800 “System Verilog” in voting stage & will be merged with 1364

## Slide 6: Other VHDL Standards
1076.1–1999: VHDL-AMS (Analog & Mixed-Signal Extensions)
1076.2–1996: Std. VHDL Mathematics Packages
1076.3-1997: Std. VHDL Synthesis Packages
1076.4-1995: Std. VITAL Modeling Specification (VHDL Initiative Towards ASIC Libraries)
1076.6-1999: Std. for VHDL Register Transfer Level (RTL) Synthesis
1164-1993: Std. Multivalue Logic System for VHDL Model Interoperability

## Slide 7: HDLs in Digital System Design
Model and document digital systems
  Hierarchical models
    System, RTL (Register Transfer Level), Gates
  Different levels of abstraction
    Behavior, structure
Verify circuit/system design via simulation
Automated synthesis of circuits from HDL models
  using a technology library
  output is primitive cell-level netlist (gates, flip flops, etc.)

## Slide 8: Anatomy of a VHDL model
“Entity” describes the external view of a component
“Architecture” describes the internal behavior and/or structure of the component
Example:
1-bit full adder
A
B
Cin
Sum
Cout
Full Adder

## Slide 9: Example: 1-Bit Full Adder
entity full_add1 is
port ( -- I/O ports
a: in bit; -- addend input
b: in bit; -- augend input
cin: in bit; -- carry input
sum: out bit; -- sum output
cout: out bit); -- carry output
end full_add1 ;
Comments follow double-dash
Type of signal
Signal direction (mode)
Signal name
I/O Port
Declarations

## Slide 10: Port Format: name: direction data_type;
Direction
  in - driven into the entity from an external source (can read, but not update within architecture)
  out - driven from within the entity
  (can drive but not read within architecture)
  inout – bidirectional; drivers both within the entity and external
  (can read or write within architecture)
  buffer – like “out” but can read and write
Data_type: any scalar or aggregate signal type

## Slide 12: 8-bit adder - entity
-- Cascade 8 1-bit adders for 8-bit adder
entity Adder8 is
port (A, B: in BIT_VECTOR(7 downto 0);
Cin: in BIT;
Cout: out BIT;
Sum: out BIT_VECTOR(7 downto 0));
end Adder8;

## Slide 13: Built-in Data Types
Scalar (single-value) signal types:
  bit – values are ‘0’ or ‘1’
  boolean – values are TRUE and FALSE
  integer - values [-231 … +(231-1)] on 32-bit host
Aggregate (multi-value) signal types:
  bit_vector – array of bits
signal b: bit_vector(7 downto 0);
signal c: bit_vector(0 to 7);
b <= c after 1 ns;
c <= “01010011”;

## Slide 14: IEEE std_logic_1164 package
-- Provides additional logic states as data values
package Part_STD_LOGIC_1164 is
type STD_ULOGIC is ( 'U', -- Uninitialized
'X', -- Forcing Unknown
'0', -- Forcing 0
'1', -- Forcing 1
'Z', -- High Impedance
'W', -- Weak Unknown
'L', -- Weak 0
'H', -- Weak 1
'-' -- Don't Care);
type STD_ULOGIC_VECTOR is array (NATURAL range <>) of STD_ULOGIC;
--others subtypes: X01,X01Z,UX01,UX01Z – subsets of std_logic/ulogic

## Slide 15: VHDL “Package”
Package = file of type definitions, functions, procedures to be shared across VHDL models
  User created
  Standard lib’s/3rd party – usually distributed in “libraries”
package name is
--type, function, procedure declarations
end package name;
package body name is -- only if functions to be defined
-- function implementations
end package body name;

## Slide 16: Bus resolution
Most commonly used data type in system design for synthesis is STD_LOGIC
function resolved (s : STD_ULOGIC_VECTOR) return STD_ULOGIC;
subtype STD_LOGIC is resolved STD_ULOGIC;
type STD_LOGIC_VECTOR is array (NATURAL range <>) of STD_LOGIC;

## Slide 17: Bus resolution function
std_logic includes a “bus resolution function” to determine the signal state where there are multiple drivers
 | ‘0’ | ‘1’ | ‘Z’ | ‘X’
‘0’ | ‘0’ | ‘X’ | ‘0’ | ‘X’
‘1’ | ‘X’ | ‘1’ | ‘1’ | ‘X’
‘Z’ | ‘0’ | ‘1’ | ‘Z’ | ‘X’
‘X’ | ‘X’ | ‘X’ | ‘X’ | ‘X’
Driver
A
Driver
B
Driver B value
Driver A value
Resolved
Bus
Value

## Slide 18: Example: 1-Bit Full Adder
library ieee; --supplied library
use ieee.std_logic_1164.all; --package of definitions
entity full_add1 is
port ( -- I/O ports
a: in std_logic; -- addend input
b: in std_logic; -- augend input
cin: in std_logic; -- carry input
sum: out std_logic; -- sum output
cout: out std_logic); -- carry output
end full_add1 ;

## Slide 19: Example: 8-bit full adder
-- 8-bit inputs/outputs
entity full_add8 is
port ( a: in std_logic_vector(7 downto 0);
b: in std_logic_vector(7 downto 0);
cin: in std_logic;
sum: out std_logic _vector(7 downto 0);
cout: out std_logic);
end full_add8 ;

## Slide 20: User-Defined Data Types
Any abstract data type can be created
Examples:
type mnemonic is (add,sub,mov,jmp);
signal op: mnemonic;
type byte is array(0 to 7) of bit;
signal dbus: byte;
Subtype of a previously-defined type:
subtype int4 is integer range 0 to 15;
subtype natural is integer range 0 to integer’high;

## Slide 21: Miscellaneous – for register transfer design
“Alias” for existing elements
signal instruction: bit_vector(0 to 31);
alias opcode: bit_vector(0 to 5) is instruction(0 to 5);
alias rd: bit_vector(0 to 4) is instruction(6 to 10);
alias rs: bit_vector(0 to 4) is instruction(11 to 15);
Fill a vector with a constant (right-most bits):
A <= (‘0’,’1’,’1’, others => ‘0’);
A <= (others => ‘0’); -- set to all 0
B(15 downto 0) <= C(15 downto 0);
B(31 downto 16) <= (others => C(15)); -- sign extension!
Concatenate bits and bit_vectors
A <= B & C(0 to 3) & “00”; -- A is 16 bits, B is 10 bits

## Slide 22: Architecture defines function/structure
entity Half_Adder is
port (X, Y : in BIT := '0';
Sum, Cout : out BIT); -- formals
end;
architecture Behave of Half_Adder is
begin
Sum <= X xor Y; -- use formals from entity
Cout <= X and Y;
end Behave;

## Slide 23: Behavioral architecture example (no circuit structure specified)
architecture dataflow of full_add1 is
begin
sum <= a xor b xor cin after 1 ns;
cout <= (a and b) or (a and cin) or
(b and cin) after 1 ns;
end;

## Slide 24: Example using an internal signal
architecture dataflow of full_add1 is
signal x1: std_logic; -- internal signal
begin
x1 <= a xor b after 1 ns;
sum <= x1 xor cin after 1 ns;
cout <= (a and b) or (a and cin) or
(b and cin) after 1 ns;
end;

## Slide 25: VHDL Signals and Simulation
Signal assignment statement creates a “driver” for the signal
  An “event” is a time/value pair for a signal change
  Ex. (‘1’, 5 ns) – Signal assigned value ‘1’ at current time + 5ns
  Driver contains a queue of pending events
  Only one driver per signal (except for special buses) – can only drive signal at one point in the model

## Slide 26: Signal assignment statement
Model signal driven by a value (signal value produced by “hardware”)
a <= b and c after 1 ns;
  Data types must match (strongly typed)
  Delay can be specified (as above)
  Infinitesimally small delay “delta” inserted if no delay specified:
a <= b and c;
  Signals cannot change in zero time!
  Delay usually unknown in behavioral & RTL models and therefore omitted

## Slide 27: Concurrent Statements and Event-Driven Simulation
Statements appear to be evaluated concurrently
Time held constant during statement evaluation
Each statement affected by a signal event at time T is evaluated
Any resulting events are “scheduled” in the affected signal driver
New values take effect when time advances to the scheduled event time

## Slide 28: Event-Driven Simulation Example
a <= b after 1ns;
c <= a after 1ns;
Time a b c
T ‘0’ ‘0’ ‘0’
T+1 ‘0’ ‘1’ ‘0’ - external event on b
T+2 ‘1’ ‘1’ ‘0’ - resulting event on a
T+3 ‘1’ ‘1’ ‘1’ - resulting event on c

## Slide 29: Structural architecture example (no behavior specified)
architecture structure of full_add1 is
component xor -- declare component to be used
port (x,y: in bit;
z: out bit);
end component;
for all: xor use entity work.xor(eqns); -- if multiple arch’s
signal x1: bit; -- signal internal to this component
begin
G1: xor port map (a, b, x1); -- instantiate 1st xor gate
G2: xor port map (x1, cin, sum); -- instantiate 2nd xor gate
…add circuit for carry output…
end;
A
B
X1
Sum
Cin

## Slide 30: Example: adder behavioral model
entity adder is
port ( a: in integer;
b: in integer;
sum: out integer);
end adder ;
architecture behave of adder is
begin
sum <= a + b; -- adder to be synthesized
end;

## Slide 31: Example: D flip-flop
entity DFF is
port (Preset: in bit;
Clear: in bit;
Clock: in bit;
Data: in bit;
Q: out bit;
Qbar: out bit);
end DFF;
Data
Clock
Q
Qbar
Preset
Clear

## Slide 32: 7474 D flip-flop equations
architecture eqns of DFF is
signal A,B,C,D: bit;
signal QInt, QBarInt: bit;
begin
A <= not (Preset and D and B) after 1 ns;
B <= not (A and Clear and Clock) after 1 ns;
C <= not (B and Clock and D) after 1 ns;
D <= not (C and Clear and Data) after 1 ns;
Qint <= not (Preset and B and QbarInt) after 1 ns;
QBarInt <= not (QInt and Clear and C) after 1 ns;
Q <= QInt;
QBar <= QBarInt;
end;

## Slide 33: 4-bit Register (Structural Model)
entity Register4 is
port ( D: in bit_vector(0 to 3);
Q: out bit_vector(0 to 3);
Clk: in bit;
Clr: in bit;
Pre: in bit);
end Register4;
D(3)
Q(3)
D(2)
D(1)
D(0)
Q(2)
Q(1)
Q(0)
CLK
PRE
CLR

## Slide 34: Register Structure
architecture structure of Register4 is
component DFF -- declare library component to be used
port (Preset: in bit;
Clear: in bit;
Clock: in bit;
Data: in bit;
Q: out bit;
Qbar: out bit);
end component;
signal Qbar: bit_vector(0 to 3); -- dummy for unused FF output
begin -- Signals connected to ports in order listed above
F3: DFF port map (Pre, Clr, Clk, D(3), Q(3), Qbar(3));
F2: DFF port map (Pre, Clr, Clk, D(2), Q(2), Qbar(2));
F1: DFF port map (Pre, Clr, Clk, D(1), Q(1), Qbar(1));
F0: DFF port map (Pre, Clr, Clk, D(0), Q(0), Qbar(0));
end;

## Slide 35: Register Structure (short cut – “generate” statement)
begin
for k in 0 to 3 generate
F: DFF port map (Pre, Clr, Clk, D(k), Q(k), Qbar(k));
end generate;
end;
Generates multiple copies of the given statement(s)
Value of k inserted where specified
Iteration number k is appended to each label F
Result is identical to previous example

## Slide 36: Conditional Signal Assignment
signal a,b,c,d,y: bit;
signal S: bit_vector(0 to 1);
begin
with S select
y <= a after 1 ns when “00”,
b after 1 ns when “01”,
c after 1 ns when “10”,
d after 1 ns when “11”;
(or: d after 1 ns when others;)
00
01
10
11
a
b
c
d
S
y
4-to-1 Mux

## Slide 37: 32-bit-wide 4-to-1 multiplexer
signal a,b,c,d,y: bit_vector(0 to 31);
signal S: bit_vector(0 to 1);
begin
with S select
y <= a after 1 ns when “00”,
b after 1 ns when “01”,
c after 1 ns when “10”,
d after 1 ns when “11”;
a,b,c,d,y can be any type, as long as they are the same
00
01
10
11
a
b
c
d
S
y
4-to-1 Mux

## Slide 38: Conditional Signal Assignment – Alternate Format
y <= a after 1 ns when (S=“00”) else
b after 1 ns when (S=“01”) else
c after 1 ns when (S=“10”) else
d after 1 ns;
Any boolean expression can be
used for each condition.
Ex. y <= a after 1 ns when (F=‘1’) and (G=‘0’) …
00
01
10
11
a
b
c
d
S
y
4-to-1 Mux

## Slide 39: Tristate buffer example (incorrect)
library ieee;
use ieee.std_logic_1164.all;
entity tristate is
port ( a: in bit;
y: out std_logic;
en: in bit);
end tristate;
architecture a1 of tristate is
begin
y <= a after 1 ns when (en=‘1’) else
‘Z’ after 1 ns;
end;
Type mismatch between y and a
y
a
en

## Slide 40: Tristate buffer example (correct)
library ieee;
use ieee.std_logic_1164.all;
entity tristate is
port ( a: in bit;
y: out std_logic;
en: in bit);
end tristate;
architecture a1 of tristate is
begin
y <= ‘0’ after 1 ns when (en=‘1’) and (a=‘0’) else
‘1’ after 1 ns when (en=‘1’) and (a=‘1’) else
‘Z’ after 1 ns;
end;
y
a
en

## Slide 41: Tristate bus buffer example
library ieee;
use ieee.std_logic_1164.all;
entity tristate is
port ( a: in std_logic_vector(0 to 7);
y: out std_logic_vector(0 to 7);
en: in bit);
end tristate;
architecture a1 of tristate is
begin
y <= a after 1 ns when (en=‘1’) else
“ZZZZZZZZ” after 1 ns;
end;
y
a
en

## Slide 42: VHDL “Process” Construct
Allows conventional programming language methods to describe circuit behavior
Supported language constructs (“sequential statements”) – only allowed within a process:
  variable assignment
  if-then-else (elsif)
  case statement
  while (condition) loop
  for (range) loop

## Slide 43: Process Format
[label:] process (sensitivity list)
declarations
begin
sequential statements
end process;
Process statements executed once at start of simulation
Process halts at “end” until an event occurs on a signal in the “sensitivity list”

## Slide 44: Using a “process” to model sequential behavior
entity DFF is
port (D,CLK: in bit;
Q: out bit);
end DFF;
architecture behave of DFF is
begin
process(clk) -- “process sensitivity list”
begin
if (clk’event and clk=‘1’) then
Q <= D after 1 ns;
end if;
end process;
end;
Process statements executed sequentially (sequential statements)
clk’event is an attribute of signal clk which is TRUE if an event has occurred on clk at the current simulation time
D Q
CLK

## Slide 45: Alternative to sensitivity list
entity DFF is
port (D,CLK: in bit;
Q: out bit);
end DFF;
architecture behave of DFF is
begin
process -- no “sensitivity list”
begin
wait on clk; -- suspend process until event on clk
if (clk=‘1’) then
Q <= D after 1 ns;
end if;
end process;
end;
Other “wait” formats: wait until (clk’event and clk=‘1’); wait for 20 ns;
Process executes endlessly if no sensitivity list or wait statement!
D Q
CLK

## Slide 46: D latch vs. D flip-flop
entity Dlatch is
port (D,CLK: in bit;
Q: out bit);
end Dlatch;
architecture behave of Dlatch is
begin
process(D, clk)
begin
if (clk=‘1’) then
Q <= D after 1 ns;
end if;
end process;
end;
-- For latch, Q changes whenever the latch is enabled by CLK=‘1’ rather than being edge-triggered)
D Q
CLK

## Slide 47: Defining a “register” for an RTL model (not gate-level)
entity Reg8 is
port (D: in bit_vector(0 to 7);
Q: out bit_vector(0 to 7)
LD: in bit);
end Reg8;
architecture behave of Reg8 is
begin
process(LD)
begin
if (LD’event and LD=‘1’) then
Q <= D after 1 ns;
end if;
end process;
end;
D and Q can be any abstract data type
D(0 to 7)
Q(0 to 7)
LD

## Slide 48: Synchronous vs. Asynchronous Flip-Flop Inputs
entity DFF is
port (D,CLK: in bit;
PRE,CLR: in bit;
Q: out bit);
end DFF;
architecture behave of DFF is
begin
process(clk,PRE,CLR)
begin
if (CLR=‘0’) then -- CLR has precedence
Q <= ‘0’ after 1 ns;
elsif (PRE=‘0’) then -- Then PRE has precedence
Q <= ‘1’ after 1 ns;
elsif (clk’event and clk=‘1’) then
Q <= D after 1 ns; -- Only if CLR=PRE=‘1’
end if;
end process;
end;
CLR
D Q
CLK
PRE

## Slide 49: Using a “variable” to describe sequential behavior within a process
cnt: process(clk)
variable count: integer; -- internal counter state
begin -- valid only in a process
if clk=‘1’ and clk’event then
if ld=‘1’ then -- “to_integer” must be supplied
count := to_integer(Din);
elsif cnt=‘1’ then
count := count + 1;
end if;
end if; -- “to_bitvector” must be supplied
Dout <= to_bitvector(count);
end process;

## Slide 50: Modeling Finite State Machines (Synchronous Sequential Circuits)
FSM design & synthesis process:
  Design state diagram (behavior)
  Derive state table
  Reduce state table
  Choose a state assignment
  Derive output equations
  Derive flip-flop excitation equations
Synthesis steps 2-6 can be automated, given the state diagram

## Slide 51: Synchronous Sequential Circuit Model
Comb.
Logic
FFs
Inputs
x
Outputs
z
Next State
Y
Present State
y
Mealy Outputs z = f(x,y), Moore Outputs z = f(y)
Next State Y = f(x,y)
Clock

## Slide 52: Synchronous Sequential Circuit (FSM) Example

## Slide 53: FSM Example – entity definition
entity seqckt is
port (
x: in bit; -- FSM input
z: out bit; -- FSM output
clk: in bit ); -- clock
end seqckt;

## Slide 54: FSM Example - behavioral model
architecture behave of seqckt is
type states is (A,B,C); -- symbolic state names
signal curr_state,next_state: states;
begin
-- Model the memory elements of the FSM
process (clk)
begin
if (clk’event and clk=‘1’) then
pres_state <= next_state;
end if;
end process;
(continue on next slide)

## Slide 55: FSM Example - continued
-- Model the next-state and output functions of the FSM
process (x, pres_state) -- function inputs
begin
case pres_state is -- describe each state
when A => if (x = ‘0’) then
z <= ‘0’;
next_state <= A;
else -- (x = ‘1’)
z <= ‘0’;
next_state <= B;
end if;
(continue next slide for pres_state = B and C)

## Slide 56: FSM Example (continued)
when B => if (x=‘0’) then
z <= ‘0’;
next_state <= A;
else
z <= ‘1’;
next_state <= C;
end if;
when C => if (x=‘0’) then
z <= ‘0’;
next_state <= C;
else
z <= ‘1’;
next_state <= A;
end if;
end case;
end process;
end;

## Slide 57: Alternative Format for Output and Next State Functions
z <= ‘1’ when ((curr_state = B) and (x = ‘1’))
or ((curr_state = C) and (x = ‘1’))
else ‘0’;
next_state <= A when ((curr_state = A) and (x = ‘0’))
or ((curr_state = B) and (x = ‘0’))
or ((curr_state = C) and (x = ‘1’)) else
B when ((curr_state = 1) and (x = ‘1’)) else
C;

## Slide 58: System Example: 8x8 multiplier
adder (ADR)
multiplicand (M)
accumulator (A)
multiplier (Q)
controller (C)
Start Clock
Done
Input Bus
Output Bus

## Slide 59: Multiply Algorithm
A <- 0
M <- INBUS
CNT <- 0
Q <- INBUS
A <- A + M
Q(7)
A:Q <- right shift
CNT <- CNT + 1
CNT
A(0) <- sign
OUTBUS <= A
OUTBUS <= Q
1
0
<8
8
IN1
IN2
ADD
SHIFT
SIGN
OUT1
OUT2
START
DONE <- 1
HALT
0
1

## Slide 60: Multiplier – Top Level
entity multiplier is
port (INBUS: in bit_vector(0 to 7);
OUTBUS: out bit_vector(0 to 7);
CLOCK: in bit;
START: in bit;
DONE: out bit);
end multiplier;
architecture struc of multiplier is
[component declarations go here]
-- internal signals to interconnect components
signal AR, MR, QR, AD, Ain: bit_vector(0 to 7);
signal AMload, AMadd, Qload, AQshift, AQoutEn, AQoutSel: bit;
signal SignLd: bit;

## Slide 61: Multiplier – Top Level (continued)
begin
OUTBUS <= AR when AQoutEn = '1' and AQoutSel = '0' else
QR when AQoutEn = '1' and AQoutSel = '1' else
"00000000";
Ain(0) <= AD(0) when AMadd = '1' else MR(0) xor QR(7);
Ain(1 to 7) <= AD(1 to 7);
M: mreg port map (INBUS, MR, AMload);
Q: Qreg port map (INBUS, QR, AR(7), Qload, SignLd, AQshift);
A: areg port map (Ain, AR, AMadd, SignLd, AQshift, AMload);
ADR: adder port map (AR, MR, AD);
C: mctrl port map (START, CLOCK, QR(7), AMload, AMadd, Qload, AQshift,
SignLd, AQoutEn, AQoutSel, DONE);
end;

## Slide 62: Multiplicand Register (mreg)
-- simple parallel-load register
entity mreg is
port (Min: in bit_vector(0 to 7);
Mout: out bit_vector(0 to 7);
Load: in bit);
end mreg;
architecture comp of mreg is
begin
process (Load) -- wait for change in Load
begin
if Load = '1' then
Mout <= Min; -- parallel load
end if;
end process;
end;

## Slide 63: Accumulator Register (areg)
-- shift register with clear and parallel load
entity Areg is
port (Ain: in bit_vector(0 to 7);
Aout: out bit_vector(0 to 7);
Load: in bit; -- load entire register
Load0: in bit; -- load a0 only
Shift: in bit; -- shift right
Clear: in bit); -- clear register
end Areg;
architecture comp of areg is
signal A: bit_vector(0 to 7); -- internal state

## Slide 64: Accumulator Register (areg)
begin
Aout <= A; -- internal value to outputs
process (Clear, Load, Load0, Shift) -- wait for event
begin
if Clear = '1' then
A <= "00000000"; -- clear register
elsif Load = '1' then
A <= Ain; -- parallel load
elsif Shift = '1' then
A <= '0' & A(0 to 6); -- right shift
elsif Load0 = '1' then
A(0) <= Ain(0); -- load A(0) only
end if;
end process;
end;

## Slide 65: Multiplier/Product Register (Qreg)
-- shift register with parallel load
entity Qreg is
port (Qin: in bit_vector(0 to 7);
Qout: out bit_vector(0 to 7);
SerIn: in bit; -- serial input for shift
Load: in bit; -- parallel load
Clear7: in bit; -- clear bit 7
Shift: in bit); -- right shift
end Qreg;
architecture comp of qreg is
signal Q: bit_vector(0 to 7); -- internal storage

## Slide 66: Multiplier/Product Register (Qreg)
begin
Qout <= Q; -- drive output from internal storage
process (Load, Shift, Clear7) -- wait for event
begin
if Load = '1' then
Q <= Qin; -- load Q
elsif Shift = '1' then
Q <= SerIn & Q(0 to 6); -- shift Q right
elsif Clear7 = '1' then
Q(7) <= '0'; -- clear bit Q(7)
end if;
end process;
end;

## Slide 67: 8-bit adder (behavioral)
use work.qsim_logic.all; -- contains bit_vector addition
entity adder is
port( X,Y: in bit_vector(0 to 7);
Z: out bit_vector(0 to 7));
end adder;
architecture comp of adder is
signal temp: bit_vector(0 to 8);
begin
temp <= ("00" & X(1 to 7)) + ("00" & Y(1 to 7));
Z <= temp (1 to 8);
end;

## Slide 68: Multiplier Controller
entity mctrl is
port (Start: in bit; -- start pulse
Clock: in bit; -- clock input
Q7: in bit; -- LSB of multiplier
AMload: out bit; -- load M & A registers
AMadd: out bit; -- load adder result into A
Qload: out bit; -- Load Q register
AQshift: out bit; -- shift A & Q registers
SignLd: out bit; -- load sign into A(0)
AQoutEn: out bit; -- enable output
AQoutSel: out bit; -- select A or Q for output
DONE: out bit); -- external DONE signal
end mctrl;

## Slide 69: Multiplier Controller - Architecture
architecture comp of mctrl is
type states is (Halt,In1,In2,Add,Shift,Sign,Out1,Out2);
signal State: States := Halt; -- state of the controller
begin
-- decode state variable for outputs
AMload <= '1' when State = In1 else '0';
Qload <= '1' when State = In2 else '0';
AMadd <= '1' when State = Add and Q7 = '1' else '0';
AQshift <= '1' when State = Shift else '0';
AQoutSel <= '1' when State = Out2 else '0';
SignLd <= '1' when State = Sign else '0';
AQoutEn <= '1' when State = Out1 or State = Out2 else '0';
DONE <= '1' when State = Halt else '0';

## Slide 70: Controller – State transition process
process (Clock) -- implement state machine state transitions
variable Count: integer;
begin
if Clock = '1' then
case State is
when Halt => if Start = '1' then -- wait for start pulse
State <= In1;
Count := 0;
end if;
when In1 => State <= In2; -- Read 1st operand
when In2 => State <= Add; -- Read 2nd operand
(Continued)

## Slide 71: Controller – State transition process (continued)
when Add => State <= Shift; -- Add multiplicand to accumulator
Count := Count + 1;
when Shift => if Count = 7 then -- Shift accumulator/multiplier
State <= Sign;
else
State <= Add;
end if;
when Sign => State <= Out1; -- Set sign of result
when Out1 => State <= Out2; -- Output lower half of product
when Out2 => State <= Halt; -- Output upper half of product
end case;
end if;
end process;

## Slide 72: 64K x 8 Memory Example
library ieee;
use ieee.std_logic_1164.all;
use work.qsim_logic.all; -- package with to_integer() func
entity memory8 is
port (dbus: inout std_logic_vector(0 to 7);
abus: in std_logic_vector(0 to 15);
ce: in bit; -- active low chip enable
oe: in bit; -- active low output enable
we: in bit); -- active low write enable
end memory8;

## Slide 73: 64K x 8 Memory Example
architecture reglevel of memory8 is
begin
process (ce,oe,we,abus,dbus)
type mem is array(natural range <>) of std_logic_vector(0 to 7);
variable M: mem(0 to 65535);
begin
if (ce='0') and (oe='0') then -- read enabled
dbus <= M(to_integer(abus)); -- drive the bus
elsif (ce='0') and (we='0') then -- write enabled
dbus <= "ZZZZZZZZ"; -- disable drivers
M(to_integer(abus)) := dbus; -- write to M
else
dbus <= "ZZZZZZZZ"; --disable drivers
end if;
end process;
end;

## Slide 74: Unconstrained Bit Vectors
Allows a generic component with different sizes:
      entity mux is
      port (a,b: in bit_vector; -- unconstrained
      c: out bit_vector;
      s: in bit );
      end mux;
      architecture x of mux is
      begin
      c <= a when (s=‘0’) else b;
      end;

## Slide 75: Unconstrained Bit Vectors
Vector constrained when instantiated:
signal s1,s2: bit;
    signal a5,b5,c5: bit_vector (0 to 4);
    signal a32,b32,c32: bit_vector (0 to 31);
    component mux
    port (a,b: in bit_vector; -- unconstrained
    c: out bit_vector;
    s: in bit );
    end component;
  begin
    M5: mux port map (a5,b5,c5,s1); -- 5-bit mux
    M32: mux port map (a32,b32,c32,s2); -- 32-bit mux