## Slide 1: VHDL Simulation
Testbench Design

## Slide 2: The Test Bench Concept

## Slide 3: Project simulations
Behavioral/RTL – verify functionality
  Model in VHDL/Verilog
  Drive with “force file” or testbench
Post-Synthesis
  Synthesized gate-level VHDL/Verilog netlist
  Technology-specific VHDL/Verilog gate-level models
  Optional SDF file (from synthesis) for timing
  Drive with same force file/testbench as in (1)
Post-Layout
  Netlist back-annotated with extracted capacitances for accurate delays

## Slide 4: Example: modulo-7 counter
VHDL Model (modulo7.vhd)
  Create working library: vlib work
  Map the lib name: vmap work work
  Compile: vcom modulo7.vhd
  Simulate: vsim modulo7(behave)
Simulation-control
  Modelsim “macro” file (mod7.do)
  Testbench (VHDL or Verilog)
ModelSim results
  List(table) and/or Waveform (logic analyzer)

## Slide 5
-- modulo7.vhd parallel-load modulo-7 synchronous counter
library ieee; use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity modulo7 is
port(reset,count,load,clk: in std_logic;
I: in std_logic_vector(2 downto 0);
Q: out std_logic_vector(2 downto 0));
end modulo7;
architecture Behave of modulo7 is
signal Q_s: unsigned(2 downto 0);
begin
process (reset,clk) begin
if (reset='0') then
Q_s <= "000";
elsif (clk'event and (clk='1')) then
if (count = '1') and (Q_s = "110") then
Q_s <= "000";
elsif (count='1') then
Q_s <= Q_s + 1;
elsif (load='1') then
Q_s <= UNSIGNED(I);
end if;
end if;
end process;
Q<=STD_LOGIC_VECTOR(Q_s);
end Behave;

## Slide 6: Test stimulus: Modelsim “do” file: mod7.do
add wave /clk /reset /count /load
add wave -hex /I /Q
add list /clk /reset /count /load
add list -hex /I /Q
force /clk 0 0 ns, 1 20 ns -repeat 40 ns
force /I 101 0 ns, 011 400 ns
force /reset 1 0 ns, 0 10 ns, 1 20 ns
force /count 0 0 ns, 1 90 ns, 0 490 ns
force /load 0 0 ns, 1 30 ns, 0 70 ns
run 600 ns

## Slide 7: Results in list format
Note “delta”
delays for
behavioral
model.

## Slide 8: Results in wave format

## Slide 9: Elements of a VHDL/Verilog testbench
Unit Under Test (UUT) – or Device Under Test (DUT)
  instantiate one or more UUT’s
Stimulus of UUT inputs
  algorithmic
  from arrays
  from files
Checking of UUT outputs
  assertions
  write to files

## Slide 10: Instantiating the UUT
-- 32 bit adder testbench
entity adder_bench is -- no top-level I/O ports
end adder_bench;
architecture test of adder_bench is
component adder is -- declare the UUTs
port (
X,Y: in std_logic_vector(31 downto 0);
Z: out std_logic_vector(31 downto 0)
);
signal A,B,Sum: std_logic_vector(31 downto 0); --internal signals
begin
UUT: adder port map (A,B,Sum); --instantiate the adder

## Slide 11: Example – stimulating clock inputs
-- Simple 50% duty cycle clock
clk <= not clk after T ns; -- T is constant or defined earlier
-- Clock process, using “wait” to suspend for T1/T2
process begin
clk <= ‘1’; wait for T1 ns; -- clk high for T1 ns
clk <= ‘0’; wait for T2 ns; -- clk low for T2 ns
end process;
-- Clock “procedure” (define in declaration area or in a package)
procedure Clock (signal C: out bit; HT, LT: TIME) is begin
loop -- schedule “waveform” on C and suspend for period
C <= ‘1’ after LT, ‘0’ after LT + HT; wait for LT + HT;
end loop;
end procedure;
-- “execute” clock procedure by instantiating it in the architecture
C1: Clock (CLK, 10ns, 8 ns);

## Slide 12: Algorithmic generation of stimulus
-- Generate test values for an 8-bit adder inputs A & B
process begin
for m in 0 to 255 loop -- all 8 bit addend values
for n in 0 to 255 loop -- all 8 bit augend values
A <= to_std_logic(m); -- apply m to adder input A
B <= to_std_logic(n); -- apply n to adder input B
wait for T ns; -- allow time for addition
assert (to_integer(Sum) = (m + n)) -- expect Sum = A + B
report “Incorrect sum” severity note;
end loop; end loop;
end process;

## Slide 13: Sync patterns with clock transitions
-- Test 4x4 bit multiplier algorithm
process begin
for m in 0 to 15 loop;
for n in 0 to 15 loop;
A <= to_std_logic(m); -- apply multiplier
B <= to_std_logic(n); -- apply multiplicand
wait until CLK’EVENT and CLK = ‘1’; -- clock in A & B
wait for 1 ns; -- move next change past clock edge
Start <= ‘1’, ‘0’ after 20 ns; -- pulse Start signal
wait until Done = ‘1’; -- wait for end of multiply
wait until CLK’EVENT and CLK = ‘1’; -- finish last clock
end loop; end loop; end process;

## Slide 14: Reading test patterns from files
use std.textio.all; -- Contains file/text support
architecture m1 of bench is begin
signal Vec: std_logic_vector(7 downto 0); -- test vector
process
file P: text open read_mode is "testvecs"; -- test vector file
variable LN: line; -- temp variable for file read
variable LB: bit_vector(31 downto 0); -- for read function
begin
while not endfile(P) loop -- Read vectors from data file
readline(P, LN); -- Read one line of the file (type “line”)
read(LN, LB); -- Get bit_vector from line
Vec <= to_stdlogicvector(LB); -- Vec is std_logic_vector
end loop; end process;

## Slide 15: Test vectors from an array
type vectors is array (1 to N) of std_logic_vector(7 downto 0);
signal V: vectors := -- initialize vector array
(
"00001100 “, -- pattern 1
"00001001“, -- pattern 2
"00110100", -- pattern 3
. . . .
"00111100“ -- pattern N
);
begin
A <= V(i); -- set A to ith vector

## Slide 16: Check results with assertions
-- Assert statement checks for expected condition
assert (A = (B + C)) -- expect A = B+C (any boolean condition)
report “Error message”
severity NOTE;
-- Print “Error message” if assert condition FALSE
(condition is not what we expected)
-- Specify one of four severity levels:
NOTE, WARNING, ERROR, FAILURE
-- Modelsim allows selection of severity level that should
halt the simulation
-- Severity level NOTE generally should not stop simulation

## Slide 17: Check timing constraints
-- Tsu for flip flop D input before clock edge is 2ns
assert not (CK’stable and (CK = ‘1’) and not D’stable(2ns))
report “Setup violation: D not stable for 2ns before CK”;
-- DeMorgan equivalent
assert CK’stable or (CK = ‘0’) or D’stable(2ns)
report “Setup violation: D not stable for 2ns before CK”;

## Slide 18: Testbench: modulo7_bench.vhd
LIBRARY ieee;
USE ieee.std_logic_1164.all;
USE ieee.numeric_std.all;
ENTITY modulo7_bench is end modulo7_bench;
ARCHITECTURE test of modulo7_bench is
component modulo7
PORT (reset,count,load,clk: in std_logic;
I: in std_logic_vector(2 downto 0);
Q: out std_logic_vector(2 downto 0));
end component;
for all: modulo7 use entity work.modulo7(Behave);
signal clk : STD_LOGIC := '0';
signal res, cnt, ld: STD_LOGIC;
signal din, qout: std_logic_vector(2 downto 0);
begin
-- instantiate the component to be tested
UUT: modulo7 port map(res,cnt,ld,clk,din,qout);
Alternative
to “do” file
Continue on
next slide

## Slide 19: Testbench: modulo7_bench.vhd
clk <= not clk after 10 ns;
P1: process
variable qint: UNSIGNED(2 downto 0);
variable i: integer;
begin
qint := "000";
din <= "101"; res <= '1';
cnt <= '0'; ld <= '0';
wait for 10 ns;
res <= '0'; --activate reset for 10ns
wait for 10 ns;
assert UNSIGNED(qout) = qint
report "ERROR Q not 000"
severity WARNING;
res <= '1'; --deactivate reset
wait for 5 ns; --hold after reset
ld <= '1'; --enable load
wait until clk'event and clk = '1';
qint := UNSIGNED(din); --loaded value
wait for 5 ns; --hold after load
ld <= '0'; --disable load
cnt <= '1'; --enable count
for i in 0 to 20 loop
wait until clk'event and clk = '1';
assert UNSIGNED(qout) = qint
report "ERROR Q not Q+1"
severity WARNING;
if (qint = "110") then
qint := "000"; --roll over
else
qint := qint + "001"; --increment
end if;
end loop;
end process;
Print message if incorrect result
qint = expected outputs of UUT