ELEC 5200-001/6200-001 (Spring 2013)

Homework 2 Problems

Assigned 2/4/13, due 2/8/12

Problem 1: Write the MIPS instructions that produce the following binary code. Interpret the action of each instruction:

- 000000 01001 01000 00000 00000 100000

- 000000 00000 01001 00000 01010 000000

- 000000 00000 00000 00000 00000 000000

Problem 2: Consider a MIPS pseudoinstruction that initializes registers 8 through 15 to 0. How will an assembler expand this into “real” instructions?

Problem 3: The following pseudoinstruction interchanges the contents of registers $r1 and $r2:

swap	$s1, $s2

How should a MIPS assembler translate it into real instructions?

# Problem 4: Implement a pseudoinstruction to copy data from a memory location whose address is in $src register to another memory location whose address is in $dst register:

mcopy		$dst, $src		# M($dst) ← M($src)

Problem 5:

- Add comments to the following MIPS code. Assume that $a0 and $a1 are used for inputs and initially contain positive integers 6 and 10, respectively. Assume that $v0 is used for output.

add	$t0,	$zero,	$zero

loop		beq	$a1,	$zero,	exit

add	$t0,	$t0,	$a0

addi	$a1,	$a1,	–1

j	loop

exit		addi	$t0,	$t0,	– 59

add	$v0,	$t0,	$zero

- What is the final value of the integer in $v0?

Problem 6: A program uses registers 16 through 25. It calls a procedure. Write the instructions that compiler should include in the program before and after the call.