ELEC 5200-001/6200-001 (Spring 2014)

Homework 3 Solution

Assigned 2/28/14, due 3/7/14

# Problem 1: Execution times of hardware blocks of a single cycle datapath are as follows:

# Multiplexer			  		  1ps

# Control					  3ps

# Register file read or write			15ps

# Sign extension			  		  1ps

# Shift left by 2			  		  1ps

# Adder or ALU					25ps

# Instruction/data memory read or write	20ps

# All other hardware times can be neglected. Find a lower bound on the cycle time for the program counter.

# Problem 2: Consider the hardware times of major units (others being negligible) in a datapath as:

# Memory access (read or write)	50ps

# ALU					75ps

# Register file (read or write)		50ps

# Determine minimum clock cycle time, average CPI, and average instruction execution time for single-cycle and multi-cycle datapaths for the following program statistics:

| Instruction type | Percentage in the program | Clock cycles used by instruction |
| --- | --- | --- |
|  |  | Single-cycle | Multi-cycle |
| lw | 10 | 1 | 5 |
| sw | 10 | 1 | 4 |
| branch | 20 | 1 | 3 |
| jump | 20 | 1 | 2 |
| register | 40 | 1 | 4 |

Problem 3:

# Suppose operations involving register file, memory or ALU take 1 time unit each. Neglecting the time of all other hardware, how much time will each MIPS instruction take on a single-cycle datapath? Consider R-type, lw, sw, beq and j instructions.

# What will be the execution times for MIPS instructions on a 5-cycle multi-cycle datapath using a clock period of 1 time unit?

# A program contains the following mix of instructions:

# lw			15%

# sw			10%

# R-type			45%

# Branch			20%

# Jump			10%

# What is the single-cycle CPU time to multicycle CPU time ratio for running this program on the two datapaths?

Problem 4: Consider two types of MIPS datapaths. The clock rates for single-cycle and multicycle implementations are 250MHz and 1GHz, respectively. The following subroutine is used for estimating the performances. The argument register $a0 contains a very large positive integer (assume several million):

repeat		addi	$a0, $a0, –1

bne	$a0, $zero, repeat

add	$v0, $a0, $zero

Determine:

(a) Average cycles per instruction (CPI) for two datapaths.

(b) How much faster is the multicycle execution of the program (ratio of single-cycle to multicycle execution times)?

Problem 5:	A multicycle datapath is implemented for an ISA that has five types of instructions. Besides the fetch and decode cycles, clock cycles used are as follows:

| Instruction class | Clock cycles for completion beyond fetch and decode | Opcode |
| --- | --- | --- |
| Type 1 | 1 | OP1 |
| Type 2 | 2 | OP2 |
| Type 3 | 3 | OP3 |
| Type 4 | 4 | OP4 |
| Type 5 | 5 | OP5 |

Sketch a state diagram for the control finite state machine. Label states and label state transitions with inputs.