ELEC 5200-001/6200-001 (Spring 2014)

Homework 4 Solution

Assigned 3/24/14, due 3/31/14

# Problem 1: Assume that each pipeline register and the program counter have a delay of 10ps. Times taken by other major hardware units in a MIPS processor are:

Memory read or write		75ps

Register file read and write	50ps

ALU				100ps

Add unit			100ps

All other hardware, including the control and multiplexers, has negligible delays. Then,

# What is the maximum clock frequency for a five-stage MIPS pipeline datapath?

# Neglecting any hazards and resulting stalls, what are the pipeline latency and the cycles per instruction (CPI) for a long instruction sequence?

# Compare this datapath with a single cycle MIPS datapath using similar hardware:

| Datapath | Clock cycle time | Clock frequency | CPI | Time per instruction | Million instructions per second (mips) |
| --- | --- | --- | --- | --- | --- |
| Single-cycle |  |  |  |  |  |
| Pipeline |  |  |  |  |  |

# Problem 2: Consider a single-cycle datapath as a one-stage pipeline. It consists of combinational and asynchronous circuitry and a single clocked register, the program counter. Its total cycle time consists of an interval q required by the register and an interval h used by the rest of the circuitry:

# Assume that the hardware delay h can be partitioned into n equal stages separated by clocked registers each having a delay q, the first stage register being the program counter. Neglecting the latency and any hazard penalties, compute the execution time of an instruction by this n-stage pipeline.

# Show that the performance limit for the pipeline when we neglect the latency and hazards is determined by the register delay q. Find an upper bound for the clock frequency for this pipeline datapath.

# For an n-stage pipeline, suppose the average hazard penalty is α(n – 1) cycles per instruction, where 0 < α < 1.0 and n ≥ 1. Find the optimum number of pipeline stages.

# For a hardware design it is estimated that h = 4×q and for the ISA, α ≈ 0.2, what is the optimum number of stages for this pipeline and what is the corresponding speed up over a single-cycle datapath?

# For q = 50ps, tabulate clock cycle time, clock rate, average CPI and performance in million instructions per second (mips) for single-cycle datapath and the pipeline datapath with optimum number of stages found in (d).

Problem 3: The following MIPS instruction sequence is executed on a 5-cycle pipeline datapath, which is implemented with hazard detection and forwarding units.

lw	$s1, 0($s0)

add	$t0, $t0, $s1

lw	$s2, 4($s0)

add	$t1, $t1, $s2

How many bubbles, if any, will be required? Can a compiler improve the performance?

Problem 4: A program consists of two nested loops, with a branch instruction at the end of each loop and no other branch instruction anywhere. The outer loop is executed 10 times and the inner loop 20 times. Determine the prediction accuracy percentage for the three prediction strategies: (a) always predict branch not taken, (b) always predict branch taken, and (c) use a 1-bit history buffer initialized to “taken” state for each branch instruction when executed first time.

# Text boxes

h

q

Reg.