ELEC 5200-001/6200-001 (Spring 2015)

Homework 1 Problems

Assigned 1/26/15, due 2/2/15

Problem 1. What are five parts of a digital computer?

Problem 2: Define:

- Harvard architecture

- Von Neumann architecture

- Stored-program computer

- Von Neumann bottleneck

Problem 3: Identify those IAS instructions that do not access memory.

Problem 4: The following table gives an 11-word assembly code written for the IAS computer. Each word contains either 40-bit constant or two 20-bit (left-L and right-R) instructions. The data contains three 100-word integer arrays, A(I), B(I) and C(I), starting in memory locations 101, 201 and 301, respectively.

| Memory address | Instruction | Comment |
| --- | --- | --- |
| 0 | 99 | Constant N, initialized to 99 |
| 1 | 1 | Constant, set to 1 |
| 2 | 100 | Constant, set to 100 |
| 3L | LOAD M(200) | Transfer A(100) from Memory address 200 to AC |
| 3R | SUB M(300) | Place A(100) – [B(100) from Memory address 300] in AC |
| 4L | STOR M(400) | Transfer AC to C(100) at Memory address 400 |
| 4R | LOAD M(0) | Load N in AC |
| 5L | SUB M(1) | Decrement N in AC by 1 |
| 5R | JUMP + M(6, 20:39) | Test N, if N ≥ 0, jump to 6R to continue |
| 6L | HALT | Halt otherwise |
| 6R | STOR M(0) | Update N in Memory address 0 |
| 7L | ADD M(1) | Increment AC by 1 |
| 7R | ADD M(2) |  |
| 8L | STOR M(3, 8:19) | Modify memory address in 3L |
| 8R | ADD M(2) |  |
| 9L | STOR M(3, 28:39) | Modify memory address in 3R |
| 9R | ADD M(2) |  |
| 10L | STOR M(4, 8:19) | Modify memory address in 4L |
| 10R | JUMP M(3, 0:19) |  |

Examine the assembly code and determine what result it produces.

Problem 5: Write the machine code (binary) for the program in Problem 4.

Problem 6: (a) What is Turing test? (b) State incompleteness theorem.