ELEC 5200-001/6200-001 (Spring 2015)

Homework 2 Problems

Assigned 2/11/15, due 2/18/15

Problem 1: Which MIPS instructions produce the following binary code. Interpret the action of each instruction:

- 000000 00000 01000 01000 00000 100000

- 000000 00000 01001 00000 00010 000000

- 000000 00000 00000 00000 00000 000000

Problem 2: Consider the MIPS pseudoinstruction,

itemp	int

where int is an integer. It initializes all temporary registers to int. How will an assembler expand this into “real” instructions?

Problem 3: The following pseudoinstruction interchanges the contents of registers $s1 and $s2:

swap	$s1, $s2

How should a MIPS assembler translate it into real instructions?

# Problem 4: Implement a pseudoinstruction to double the value of data in a memory location whose address is in $reg:

m2		$reg		# M($reg) ← M($reg) × 2

Problem 5:

- Add comments to the following MIPS subroutine code. Assume that $a0 and $a1 are used for input arguments and initially contain positive integers 5 and 10, respectively. Register $v0 is used for returning the result.

add	$t0,	$0,	$0

loop		beq	$a1,	$0,	exit

add	$t0,	$t0,	$a0

addi	$a1,	$a1,	–1

j	loop

exit		addi	$t0,	$t0,	– 49

add	$v0,	$t0,	$t0

- What are the contents of registers $v0, $a0 and $a1 when the subroutine returns?

Problem 6: A program uses registers 15 through 24. It calls a procedure. Write the instructions that compiler should include in the program before and after the call.