# ELEC 5270/ELEC 6270 Low-Power Design of Electronic Circuits

# Final Exam, May 7, 2009						Total 25 points

# Broun 125, 4:00-6:30PM

Instructions: Please read all problems before writing your answers. Attempt all five problems. Be sure to revise your answers before turning them in. Please number your answer sheets, and on the first page identify the test as shown above, write your name and the total number of pages, and staple them before submitting. One point is reserved for neatness. Thank you.

Problem 1:									6 points

For the power management techniques listed in table below, specify the influence on power and energy as “reduced”, “increased” or “unchanged”.

| Power management technique | Power | Energy per clock cycle |
| --- | --- | --- |
|  | Dynamic | Static (leakage) | Dynamic | Static (leakage) |
| Clock gating |  |  |  |  |
| Clock frequency down-scaling |  |  |  |  |
| Power gating (sleep mode) |  |  |  |  |
| Voltage down-scaling |  |  |  |  |
| Parallelism with voltage scaling |  |  |  |  |

Problem 2:									6 points

Following data are given for a CMOS processor whose supply voltage is V (greater than the threshold voltage of 0.4 volt) and clock frequency is f:

(a) Dynamic power = CV2f/2 watt, where C = 50nF is the average capacitance switched per cycle and f is in GHz.

(b) Leakage power = GV2 watt, where G = 25 mho is the total leakage conductance.

(c) The alpha-power law for maximum frequency gives f = (V – 0.4)/V GHz.

(d) Short circuit power is negligible.

Find the supply voltage and clock frequency for minimum per cycle energy consumption.

What is the energy saving that this operating condition provides over the rated 1 volt maximum clock frequency operation of the processor?

Problem 3:									6 points

The processor of problem 2 is redesigned in a low leakage technology, such that G ≈ 0 and the alpha-power law for maximum clock frequency gives, f = (V – 0.5)2/V GHz. The rated supply voltage is 2.0 volt. What should be the supply voltages for (a) dual core, (b) quad core and (c) eight-core designs? What are respective power ratios with respect to the rated-voltage design? Neglect short circuit power and leakage and assume 10% overhead for each additional core.

Problem 4:										6 points

(a) In a CMOS technology all pMOS and nMOS transistors are designed to have identical “off” resistance of 1MΩ. In comparison, their “on” resistances are negligible. For a supply voltage of 1 volt, find the leakage current of a two-input NAND gate as a function of its input logic states.

(b) Construct a 2-to-1 multiplexer using four two-input NAND gates. Tabulate all input vectors and their leakage currents. Identify a minimum leakage vector (MLV) and a maximum leakage vector and specify their corresponding leakage currents.

Problem 5 (Bonus Question):						2 points

Explain what purpose the CMOS transmission gate serves in the following implementation of exclusive-OR function. Can the circuit work without the CMOS transmission gate?

# Text boxes

AB’ +A’B

B

A