(

Low power Linear Feedback Shift Register with clock gating

Ahmed Faraz, Graduate student, Department of Electrical and Computer Engineering, Auburn University, Dr. Vishwani D. Agrawal, James J. Danaher Professor, Auburn University

Abstract— A modified Linear Feedback Shift Register is designed in which power consumption is reduced by deactivating the clock signal to Flip Flop when the output signal is not different from input signal. The power consumption of the new LFSR is reduced due to the reduced switching of Flip Flop To verify, the maximum, minimum and average power of the two LFSRs are the compared.

# INTRODUCTION

TODAY, pseudo-random bit generators (PRBGs) are widely used in many electronic equipment. A good PRBG must be characterized by repeatability (i.e., giving the same output sequence when the same seed is used) and randomness. Today, hardware implementation of the PRBGs is almost always made up of the well-known linear-feedback shift register(LFSR) whose generic circuit is reported in Fig.1. This circuit is very simple to be implemented, but since the clock-path of all flip-flops (FFs) toggle at every clock cycle, they consume a significant amount of power.

In this paper, we present the gated clock design approach for LFSRs which can lead to power reduction without unduly complicating the traditionally simple topology.

# Clock Gating at register transfer level

Power should be optimized at all stages, but it is generally convenient to address it after Register Transfer Level (RTL).

RTL clock gating is the most commonly used optimization technique for improving power consumption, but depends critically on how well a design is clock gated. At this point in the design flow, designer has flexibility in the implementation to make significant improvement in the energy saving..

# TRADITIONAL LINEAR FEEDBACK SHIFT REGISTER

A linear feedback shift register (LFSR) is a shift register whose input bit is a linear function of its previous state. The only linear functions of single bits are XOR and inverse-XOR, thus it is a shift register whose input bit is driven by the exclusive-or (XOR) of some bits of the overall shift register value. As shown in Fig., it is obtained with an array of FF’s with a linear feedback performed by several XOR gates. Although LFSR’s are very simple to implement, they are based on rather complex mathematical theory [8]. However, they can be efficiently describes through the nth order polynomial

Pn(x) = xn +bn-1xn-1+ bn-2xn-2 +…….. b2x2 + b1x  +1

The bit positions that affect the next state are called the taps. In the diagram below the taps are [16,14,13,11,1]. The rightmost bit of the LFSR is called the output bit. The taps are XOR'd sequentially with the output bit and then fed back into the leftmost bit. The sequence of bits in the rightmost position is called the output stream.

16 bit Linear Feedback Shift Register

The taps of an LFSR can be represented as a polynomial mod 2. This means that the coefficients of the polynomial must be 1's or 0's. This is called the feedback polynomial or characteristic polynomial. For example, if the taps are at the 16th, 14th, 13th and 11th bits (as shown), the feedback polynomial is

The 'one' in the polynomial does not correspond to a tap — it corresponds to the input to the first bit (i.e. x0, which is equivalent to 1). The powers of the terms represent the tapped bits, counting from the left. The first and last bits are always connected as an input and tap respectively.

# Gating

To reduce power consumption in a digital system a set of strategies termed dynamic power management (DPM) is often used. The DPMs strategy consists in disabling the logic circuits that are not performing functional operations during a particular time frame, thus reducing power consumption. At circuit level, this strategy is applied by the so-called “gated clock” approach which disables the clock of FFs when output is same as input, as it is shown in Fig. 2 and activating the FF only when the input signal is different from the actual output value. As it can be easily understood, this approach is perfectly compatible with a LFSR only adding some extra gates,

# SIMULATION RESULTS

In order to evaluate the power reduction obtained by applying clock gating approach in LFSR, we have evaluated the power consumption in  16 bit Traditional LFSR and power consumption in  16 bit LFSR with clock gating for same input vector and same clock cycles.

VHDL code of traditional  16 bit LFSR was first simulated in MODELSIM and then Verilog gatenetlist was generated by Leonardo, which was then imported in Design Architect which gave the average, maximum and minimum power consumed through ELDO.

Similarly VHDL code of 16 bit LFSR with gated clock was simulated and synthesized and the power was obtained using ELDO.

Traditional 16 bit LFSR

Clock gated  16 bit LFSR

|  | WITHOUT CLOCK GATING | WITH CLOCK GATING |
| --- | --- | --- |
| Average power | 5.6966 mW | 4.913 mW |
| Maximum power | 37.939 mW | 30.144 mW |
| Minimum power | 45.6137 nW | 62.4403 nW |

Comparison between 16 bit Traditional LFSR and16 bit clock gate LFSR.

# conclusion

Reduced power Linear Feedback Shift Register with gated clock is here designed. There is 20% reduction in Maximum power, 13% reduction in Average power achieved.

In contrast to the above results, Minimum power was increased by 36%, that may be due to power consumed in initial transitions and that is in order of nano watts, which is too small as compared to power reduction in Maximum power and Average power.

References

- Qing Wu, Massoud Pedram, and Xunwei Wu, “Clock-Gating and Its Application to Low Power Design of Sequential Circuits,” 	IEEE TRANSACTIONS ON CIRCUITS AND SYSTEMS—I: FUNDAMENTAL THEORY AND APPLICATIONS, VOL. 47, NO. 103, MARCH 2000

- Walter Aloisi and Rosario Mita, Member, IEEE, Gated clock design  of Linear Feedback Shift Register , IEEE TRANSACTIONS ON CIRCUITS AND SYSTEMS—II: EXPRESS BRIEFS, VOL. 55, NO. 6, JUNE 2008

- L. Lee, S. AI-Sarawi and D. Abbott, “Low power serial parallel dynamic shift registers),” Electronics letters 9th Jnuary 2003 vol.39 no.1

- Mitch Dale, “Utilizing clock gating efficiency to reduce power EE Times- India January 2008.

- Dr. Vishwani Agrawal,” Class slides ,Low power design of electronic circuits”  Auburn University ,spring 2009.

# Footnotes

Report was submitted on April 27, 2009, as a part of  a course” Low Power Design of Electronic Circuits”

Ahmed Faraz is a graduate student in Electrical and Computer Engineering department, Auburn University, Auburn, AL 36849 USA.

Dr. Vishwani D. Agrawal is a James J. Danaher Professor in Electrical and Computer Engineering, Auburn University, Auburn, AL 36849 USA.

# Text boxes

Fig. 1.  Magnetization as a function of applied field. Note that “Fig.” is abbreviated. There is a period after the figure number, followed by two spaces. It is good practice to explain the significance of the figure in the caption.