Estimate power saving by clock slowdown for s5378 in 180nm and 32nm CMOS

Chao Han

By doing this project, we should be able to understand the influence of clock frequency in power and energy saving within one certain CMOS technology (here is 180nm and 32nm) and between these two different CMOS technology.

For a circuit, the total power consumption Ptotal = Pdyn + Pstat = Ptran + Psc + Pstat. Ptran stands for transition power, Psc stands for short circuit power, Pstat stands for static power. Ptrans = Etrans α fck = α fck CV2/2. So in the simulation we can expect transition power reduces in proportion to the reducing of clock frequency.  And the energy consumption remains that same because it equals the product of transition power and clock frequency. For short circuit power, it relates to the rise and fall times of input, the output load capacitance and the VDD, so clock frequency itself has nothing to do with it. But if we increase the output load capacitance when we slow down the clock, then we can save short circuit power. For static power, it mainly relates to the sub-threshold current. As clock frequency slows down, the power consumption remains the same, but the energy consumption would increase in proportion to the reducing of clock rate.

Below is the simulation procedure. First of all I use Matlab conversion program to convert the benchmark netlist file into rutger file which is supported by the simulation tool Powersim. Then I load 10 random vectors and the two CMOS technology parameter file as input files into the Powersim to do the simulation based on the rutger netlist file I generated before.

Belows are the simulation results:

| 180nm technology at 1.8V supply voltage |
| --- |
| Clock rate | Short circuit power | leakage power | transition power | Total power | Power saving | Energy per cycle |
| 40MHz | 0 | 4.368uW | 46.177uW | 50.545uW | 0% | 1263.6uWns |
| 20 MHz | 0 | 4.418uW | 23.089uW | 27.507uW | 45.6% | 1375.4uWns |
| 10 MHz | 0 | 4.443uW | 11.544uW | 15.987uW | 68.4% | 1598.7uWns |
| 5 MHz | 0 | 4.456uW | 5.772uW | 10.228uW | 79.8% | 2045.6uWns |
| 2.5 MHz | 0 | 4.462uW | 2.886uW | 7.348uW | 85.5% | 2939.2uwns |

| 32nm technology at 0.9V supply voltage |
| --- |
| Clock rate | Short circuit power | leakage power | transition power | Total power | Power saving | Energy per cycle |
| 40MHz | 0 | 4.368uW | 11.544uW | 15.912uW | 0% | 397.8uWns |
| 20 MHz | 0 | 4.418uW | 5.772uW | 10.190uW | 40.0% | 509.5uWns |
| 10 MHz | 0 | 4.443uW | 2.886uW | 7.329uW | 54.0% | 732.9uWns |
| 5 MHz | 0 | 4.456uW | 1.443uW | 5.899uW | 62.9% | 1179.8uWns |
| 2.5 MHz | 0 | 4.462uW | 0.722uW | 5.184uW | 67.4% | 2073.6uWns |

As we can see, short circuit power is 0 for both technologies. The reason may be among the 35 inputs of the benchmark netlist, there is no clock input. Thus only few of the gates are activated by the primary input signals; most of the gates in the circuit are not activated since the FFs are not clocked. At that time I should have saw the problem and add another input as clock input to do the simulation. Or maybe there is some problem of the tool and it is not able to estimate the short circuit power.

There is no big difference of leakage power among different clock frequency. But it is increasing very slowly as clock frequency is reducing. What I should mention is that the leakage power is the same for the two different CMOS technology. Yet actually 180nm is the low leakage power technology and 32nm is the high leakage power technology. So I guess there is something wrong in the simulation tool.

For transition power, it reduces in proportion to the reducing of clock frequency. And at high frequency modes transition power plays a main part in the total power consumption while at lower frequency leakage power becomes increasingly significant and finally contributes mainly to the total power. Another thing I should mention here is that if I divide the transition power of 180nm technology by that of 32nm technology with the same clock frequency, the result is 4. And the ratio of 1.8 and 0.9 is also 4. So I tried to do another power simulation for 32nm technology at 1.8V supply voltage and found that the transition power is same as 180nm technology at 1.8V supply voltage. However, in reality there should be some power difference between these two technologies due to the different parameters of the two technologies.

For energy saving, there is no minimum point among different clock frequencies for these two technologies. It is because for leakage energy, Ele = Pstat / f. As f slows down, Pstat remains the same, so Ele increases as clock frequency reduces. While for transition energy, Etran = Ptran / f. Ptran reduces in proportion to the reducing of f, so Etran remains that same. Thus total energy consumption increases as clock frequency slows down.

In conclusion, Clock slowdown has impact in power saving not energy saving, and it becomes not significant when frequency becomes very slow because now the leakage power plays an important part in total power consumption. For high leakage CMOS technology like 32nm, leakage power becomes extremely significant when clock frequency slows down to the level when transition power becomes very small.

References:

ELEC6270-001/5270-001 Low Power Design of Electronic Circuits slides 	Vishwani D. Agrawal

# Text boxes

Simulation result:

Dynamic power

SC power

Leakage Power

CMOS technology parameter

Vector set

Powersim

S5378 rutger netlist file

Matlab conversion program

S5378 Benchmarknetlist file