ELEC 7770-001 Advanced VLSI Design 
Spring 2007

Homework 1

Assigned 2/6/07, due 2/13/07

Problem 1. 	Consider a three-dimensional VLSI system in the form of a cube, where 			the volume contains transistors and interconnects and the pins are placed 			on the surface. Derive Rent’s rule for this device. Is the test problem for 			the cube more, or less, complex than that for the flat chip? Comment on 			the heating and cooling of the cubical device. (Note: This problem is 			similar to Problem 1.5 on page 16 in the book – M. L. Bushnell and V. D. 			Agrawal, Essentials of Electronic Testing . . .)

Problem 2.		Synthesize a 32-bit ALU circuit in 0.18μ CMOS technology using Mentor 	Graphics tools. Design the circuit two ways, for minimum area and for 	minimum delay. Tabulate number of gates, estimates of area, delay and 	power consumption, tests for stuck-at faults (numbers of faults and test 	vectors, coverage, redundant faults), tests for transition delay faults 	(numbers of faults and test vectors, coverage, untested faults), and tests for 	IDDQ (pseudo-stuck-at) faults for the two designs.