Physical Design:  Layout in Automated IC Design

-Kyungseok Kim

Following ASIC design flow (Fig.1.), front-end design consists of creating the logic for the design, simulation, and test vector generation. The logic could be automatically generated by the synthesis step, which generates gate-level netlists, with hardware description language (VHDL, Verilog). Also, It is directly designed by schematic drawing as a manual source. After having a logic source, we could use simulators and test vector generators to test the design in the gate-level. For layout, there are two types of layout procedures. One is creating an IC layout from schematics or a netlist by placing standard cells into a layout and performing automatic routing between the blocks or cells in the automated IC design. The other is manually creating and editing each polygon by the layout editors in full custom IC design.

For this design project, the layout of design will be automatically generated by placing the standard cells from a gate level netlist following the automated IC design scheme. The layout stage (Fig.2.) consists of several steps to present the design in physical device level masks under design rules which depends on each technology vendor for fabricating a real chip. In first step, library creation is the process of creating a library of standard cells that are used in the design. A cell library is a design object which contains the cells in the design. Floorplanning is the process of estimating the chip area that will be used for each standard cell or block. A floorplan is a topological structure comprised of rows and shapes used as guides for placing cells in the design. Placement is the process of placing standardcells or blocks onto the floorplan. Then, the process of placing and connecting signal and power paths between the standard cells or blocks is done the in routing stage. After routing, compaction is executed to minimize the size of a completed layout. Finally, we need to determine whether the layout conforms to the design rules, corresponds to the source schematic, and performs satisfactorily. Then, the mask layout is transferred to patterns that can be used to generate a real IC in the stage of design verification and pattern generation.

<Fig.1.> ASIC Design Flow in Dr. Nelson’s lecture note    <Fig.2.> Automated Layout Design Flow

Layout Procedure: There are two designs to demonstrate the layout stage flowing automated IC design flow in TSMC 0.18um technology. The layout for the design project of CPU is not complete with overwhelming overflows after routing step. So, alternative design (MUX) gives the example of whole layout procedure with extract parameters, lumped R and C.

Design project for CPU

-Schematic design with a symbol from logic source came from the synthesis step:

The gate level netlist of CPU can be existed as one Verilog file and handed over the layout procedure. At that time, we could layout only flat option. Then, it makes the complexity of routing and generates too many overflows which couldn’t automatically route the signal nets between the cells. We need to draw the signal nets manually to complete the layout procedure. The suggestion is that the design in synthesis step would be separated and blocked into each functional component for reducing the complexity of routing and managing the overflows.

Scan-test component is added to design by DFT tools.

<Source: CPU_areaOPt_scan.v>

- Floorplanning:

Before placing stardard-cells, Floorplan automatically generated by the tools and we could also specify the area and the internal inventories such as rows, channel, and aspect ration. The specifications of automatically generate floorplan are tabulated in the following:

| Total area | 157284512 um2 |
| --- | --- |
| # of internal rows | 55 |
| Avg. instance height | 120.0 um |
| Avg. channel height | 120.0 um |
| Total connections(pins-nets) | 44099 |
| Internal zone width | 12008.0 um |
| Internal zone height | 13204.0 um |
| Aspect ratio | 0.93 |

<Floorplan>

- Placement for Std. Cells:

Each technology package provides its own standard cells in the library. This stage places all cells which are used in the design on the floorplan. Then, all cells are connected by signal nets and ports before routing.

< Entire Design Cells >

<Zoom-In>        < Connect Ports >

- Automated routing:

For routing, there are several routing options to reduce the wire-length, the congestion of signal nets, and the overflows. For our CPU design, there are so many overflows more than 6678 after routing procedure. It could be caused to choose the flat scheme instead of the hierarchical scheme for the design. Also, the overflows depend on the algorithm of routing. Unfortunately, the layout for CPU couldn’t be completed by overflows. The considerable size of designs would be implemented by blocks hierarchically. For the benefit of hierarchical design in large circuits, a designer could manually handled more on existed problems for the correct route.

Number of Overflows: 6678

Number of Global routing nodes: 157444

Number of Global routing arcs: 201136

Check Shorts: O.K.

Alternative Design for demonstrating whole layout procedure: MUX

The verified Mux design is personally chosen to show a layout procedure without verification of functionality, because it is already proved by a VHDL code provider.

1. VHDL codes are presented in Appendix I

2. Gate level netlist are generated by the Mentor DA-IC tools in Appendix II

3. Completed layout from the Mentor IC Station

Total area = 94848.0 um2                 Number of core instances = 12

Number of signal nets  = 26              Number of power nets = 2

Number of global routing nodes = 156      Number of global routing arcs = 167

Avg. instance height = 120.0 um           Avg. channel height = 32.0 um

Aspect ratio = 1.73                          DRC & LVS Check: O.K.

4. Extract the parameters of lumped R & C and Couped C from the Mentor Calibre in Appendix III

Tip: After finishing DRC& LVS check, push Calibre in the Menu from the IC station and then, give the path ( /opt/mentor/Calibre2005.2) in Setup for executing the Calibre correctly.

Conclusion:

During the layout procedure, some problems are not expected before doing the layout with a little big circuit. Especially, automated layout has to be related to the previous stages and strategy in ASIC design flow. It is needed to keep good communications with logic level designers and solve the problems using the options which do not degrade the specification and performance of the design. After layout, we can do post-simulations for delay and power with the parameters in Mach TA (only supported by ami05, ami12, tsmc025, tsmc035). Before generating GDS II file for fabrication, we need to add pads and power lines, finally do verify DRC&LVS, and do post-simulation again for checking the expected specification in the design.

Reference:  Dr. Nelson’s lecture notes in ELEC 6250

Mentor IC Station User Manual

Mentor ADK Tutorial

Appendix I: VHDL Code for MUX

library ieee;

use ieee.std_logic_1164.all;

-------------------------------------------------

entity Mux is

port(	I3: 	in std_logic_vector(2 downto 0);

I2: 	in std_logic_vector(2 downto 0);

I1: 	in std_logic_vector(2 downto 0);

I0: 	in std_logic_vector(2 downto 0);

S:	in std_logic_vector(1 downto 0);

O:	out std_logic_vector(2 downto 0)

);

end Mux;

-------------------------------------------------

architecture behv1 of Mux is

begin

process(I3,I2,I1,I0,S)

begin

-- use case statement

case S is

when "00" =>	O <= I0;

when "01" =>	O <= I1;

when "10" =>	O <= I2;

when "11" =>	O <= I3;

when others =>	O <= "ZZZ";

end case;

end process;

end behv1;

architecture behv2 of Mux is

begin

O <=	I0 when S="00" else

I1 when S="01" else

I2 when S="10" else

I3 when S="11" else

"ZZZ";

end behv2;

Appendix II: Gate level netlist for MUX

// Verilog description for cell Mux,

// Thu Apr 23 17:01:52 2007

// LeonardoSpectrum Level 3, 2005a.82

module Mux ( I3, I2, I1, I0, S, O ) ;

input [2:0]I3 ;

input [2:0]I2 ;

input [2:0]I1 ;

input [2:0]I0 ;

input [1:0]S ;

output [2:0]O ;

wire nx2, nx18, nx84, nx87, nx89, nx93, nx95, nx98, nx100;

nand02 ix29 (.Y (O[0]), .A0 (nx84), .A1 (nx87)) ;

aoi32 ix85 (.Y (nx84), .A0 (I3[0]), .A1 (S[1]), .A2 (S[0]), .B0 (I0[0]), .B1 (nx18)) ;

nor02 ix19 (.Y (nx18), .A0 (S[1]), .A1 (S[0])) ;

aoi32 ix88 (.Y (nx87), .A0 (I1[0]), .A1 (nx89), .A2 (S[0]), .B0 (I2[0]), .B1 (nx2)) ;

inv01 ix90 (.Y (nx89), .A (S[1])) ;

nand02 ix43 (.Y (O[1]), .A0 (nx93), .A1 (nx95)) ;

aoi32 ix94 (.Y (nx93), .A0 (I3[1]), .A1 (S[1]), .A2 (S[0]), .B0 (I0[1]), .B1 (nx18)) ;

aoi32 ix96 (.Y (nx95), .A0 (I1[1]), .A1 (nx89), .A2 (S[0]), .B0 (I2[1]), .B1 (nx2)) ;

nand02 ix60 (.Y (O[2]), .A0 (nx98), .A1 (nx100)) ;

aoi32 ix99 (.Y (nx98), .A0 (I3[2]), .A1 (S[1]), .A2 (S[0]), .B0 (I0[2]), .B1 (nx18)) ;

aoi32 ix101 (.Y (nx100), .A0 (I1[2]), .A1 (nx89), .A2 (S[0]), .B0 (I2[2]), .B1 (nx2)) ;

nor02ii ix3 (.Y (nx2), .A0 (S[0]), .A1 (S[1])) ;

endmodule

Appendix III: Extract the parameters of lumped R&C and Coupled C by Calibre

LAYOUT NAME:              MUX

RULE FILE NAME:           rules

CREATION TIME:            Apr 25 18:40:16 2007

UNITS:                    Resistance  = ohm

Capacitance = farad

Time        = ns

---------------------------------------------------------------------------------

CELL NAME:                MUX

Netid      R(UpperBound)      Cvalue      %Coupled    RC(UpperBound)   Netname

---------+---------------+-------------+-------------+--------------+------------

35                    0.0   8.70736e-16             0            0.0  X142/9

- Coupled nets

- Intrinsic Capacitance

8.70736e-16

- Coupled capacitance

39                    0.0   8.57602e-16             0            0.0  X143/9

- Coupled nets

- Intrinsic Capacitance

8.57602e-16

- Coupled capacitance

43                    0.0   1.23446e-15             0            0.0  X144/9

- Coupled nets

- Intrinsic Capacitance

1.23446e-15

- Coupled capacitance

47                    0.0   8.57592e-16             0            0.0  X145/9

- Coupled nets

- Intrinsic Capacitance

8.57592e-16

- Coupled capacitance

51                    0.0   8.57592e-16             0            0.0  X146/9

- Coupled nets

- Intrinsic Capacitance

8.57592e-16

- Coupled capacitance

55                    0.0   6.05047e-16             0            0.0  X147/9

- Coupled nets

- Intrinsic Capacitance

6.05047e-16

- Coupled capacitance

1                     0.0   2.44355e-15             0            0.0  I1[2]

- Coupled nets

- Intrinsic Capacitance

2.44355e-15

- Coupled capacitance

2                     0.0   2.03613e-15             0            0.0  O[2]

- Coupled nets

- Intrinsic Capacitance

2.03613e-15

- Coupled capacitance

3                     0.0   2.67394e-15             0            0.0  I2[2]

- Coupled nets

- Intrinsic Capacitance

2.67394e-15

- Coupled capacitance

4                     0.0   2.34272e-15             0            0.0  I0[2]

- Coupled nets

- Intrinsic Capacitance

2.34272e-15

- Coupled capacitance

5                     0.0   2.64644e-15             0            0.0  I1[1]

- Coupled nets

- Intrinsic Capacitance

2.64644e-15

- Coupled capacitance

6                     0.0   1.87951e-15             0            0.0  I3[2]

- Coupled nets

- Intrinsic Capacitance

1.87951e-15

- Coupled capacitance

7                     0.0   2.51951e-15             0            0.0  I2[1]

- Coupled nets

- Intrinsic Capacitance

2.51951e-15

- Coupled capacitance

8                     0.0   2.27235e-15             0            0.0  I0[1]

- Coupled nets

- Intrinsic Capacitance

2.27235e-15

- Coupled capacitance

9                     0.0   1.87951e-15             0            0.0  I3[1]

- Coupled nets

- Intrinsic Capacitance

1.87951e-15

- Coupled capacitance

10                    0.0    2.1918e-15             0            0.0  O[1]

- Coupled nets

- Intrinsic Capacitance

2.1918e-15

- Coupled capacitance

11                    0.0   1.38136e-14             0            0.0  S[1]

- Coupled nets

- Intrinsic Capacitance

1.38136e-14

- Coupled capacitance

12                    0.0   2.55626e-15             0            0.0  I2[0]

- Coupled nets

- Intrinsic Capacitance

2.55626e-15

- Coupled capacitance

13                    0.0   2.24267e-15             0            0.0  I0[0]

- Coupled nets

- Intrinsic Capacitance

2.24267e-15

- Coupled capacitance

14                    0.0    2.4524e-15             0            0.0  I1[0]

- Coupled nets

- Intrinsic Capacitance

2.4524e-15

- Coupled capacitance

15                    0.0   1.78474e-15             0            0.0  I3[0]

- Coupled nets

- Intrinsic Capacitance

1.78474e-15

- Coupled capacitance

16                    0.0   1.95574e-15             0            0.0  O[0]

- Coupled nets

- Intrinsic Capacitance

1.95574e-15

- Coupled capacitance

17                    0.0   1.44782e-14             0            0.0  S[0]

- Coupled nets

- Intrinsic Capacitance

1.44782e-14

- Coupled capacitance

18                    0.0   3.28549e-15             0            0.0  18

- Coupled nets

- Intrinsic Capacitance

3.28549e-15

- Coupled capacitance

19                    0.0   8.36502e-15             0            0.0  19

- Coupled nets

- Intrinsic Capacitance

8.36502e-15

- Coupled capacitance

20                    0.0   3.82952e-15             0            0.0  20

- Coupled nets

- Intrinsic Capacitance

3.82952e-15

- Coupled capacitance

21                    0.0   7.60177e-15             0            0.0  21

- Coupled nets

- Intrinsic Capacitance

7.60177e-15

- Coupled capacitance

22                    0.0   7.58555e-15             0            0.0  22

- Coupled nets

- Intrinsic Capacitance

7.58555e-15

- Coupled capacitance

23                    0.0   1.80367e-14             0            0.0  GND

- Coupled nets

- Intrinsic Capacitance

1.80367e-14

- Coupled capacitance

24                    0.0   2.20344e-14             0            0.0  VDD

- Coupled nets

- Intrinsic Capacitance

2.20344e-14

- Coupled capacitance

25                    0.0    2.8993e-15             0            0.0  25

- Coupled nets

- Intrinsic Capacitance

2.8993e-15

- Coupled capacitance

26                    0.0    2.8678e-15             0            0.0  26

- Coupled nets

- Intrinsic Capacitance

2.8678e-15

- Coupled capacitance

27                    0.0   2.98647e-15             0            0.0  27

- Coupled nets

- Intrinsic Capacitance

2.98647e-15

- Coupled capacitance

28                    0.0   3.03943e-15             0            0.0  28

- Coupled nets

- Intrinsic Capacitance

3.03943e-15

- Coupled capacitance

29                    0.0   4.47234e-16             0            0.0  29

- Coupled nets

- Intrinsic Capacitance

4.47234e-16

- Coupled capacitance

# Text boxes

Overflows

Changing Options In Auto Route