ELEC 7770-001 Advanced VLSI Design 
Spring 2008

Homework 2

Assigned 2/19/08, due 2/26/08

Problem 1. Design two 8-bit combinational multiplier circuits, one for area optimization and the other for delay optimization. Create a miter circuit to apply the simulation-based heuristic to verify the logical equivalence of the two circuits – concatenate two vector sets separately generated for 100% fault coverage in the two multiplier circuits, respectively. Examine three cases of errors in one of the circuits by replacing a single gate in each case by a different type of gate. Determine whether the simulation strategy shows non-equivalence.

Problem 2. A comparator circuit compares two 2-bit vectors (a1, a2) and (b1, b2) to produce a true output only when a1 = b1 and a2 = b2. Sketch the binary decision tree and the corresponding reduced order binary decision diagram (ROBDD) for variable orders (i) a1, a2, b1, b2 and (ii) a1, b1, a2, b2.

Problem 3. Using the Elmore delay formula, show that the delay of a long interconnect increases in proportion to the square of the interconnect length. Suppose we split a long interconnect of total delay D into three equal length segments separated by two buffers, each of delay d. Show that the overall delay will be reduced provided d < D/3.