ELEC 7770-001, Spring 2008

Homework # 3 Solution

Assigned: Tuesday, Mar. 11, 2008

# Due: Tuesday, Mar. 25, 2008

Problem 1: A clock signal is routed to two edge-triggered flip-flops A and B that form a two-bit shift register. The following circuit is extracted from the layout. Find clock skews for the two flip-flops.

Problem 2: Setup time is 5ps and hold time is 3ps for each flip-flop. Assume that the clock to Q delay is the same as the hold time. To satisfy the short-path constraint, a delay buffer is inserted between the flip-flops. Find the lower bound on the clock period for the shift register.

Problem 3: Suppose we reroute the clock signal in an attempt to eliminate the buffer such that FF A is supplied the clock with larger skew and FF B the clock with smaller skew. Can the shift register work without the delay buffer? What is the clock period for the buffer-less design? Compare this design with the zero-skew design in which xA = xB.

# Text boxes

R1 = 3Ω

R2 = 8Ω

1 = 5Ω

C1 = 0.725pF

C2 = 0.725pF

Clock

source

FF A

FF B